## Slide 1: Advanced Computer Architecture
Fall 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering Amirkabir University of Technology

## Slide 2: Grading
Final Exam: 50%
Quiz: 30%
Assignments: 20%
Projects: 10%

## Slide 3: Course Outline
Introduction
Memory Hierarchy
Prefetching
Instruction-level parallelism
  Pipeline, branch prediction, out-of-order execution, …
Data-level parallelism
Vector processors and SIMD
Thread-level parallelism
  Multicores and coherency protocols

## Slide 4: Textbook
Computer Architecture: A Quantitative Approach, 6th edition, John L. Hennessy, David A. Patterson, MK pub., 2019
Processor Architecture From Dataflow to Superscalar and Beyond, Jurij Silc, Borut Robic, Theo Ungerer, Springer, 1999.
High Performance Computer Architecture, 3rd Edition Harold
S. Stone, 1987

## Slide 5: Copyright Notice
Lectures adopted from
Computer Architecture: A Quantitative Approach, 6th
edition, John L. Hennessy, David A. Patterson, MK pub., 2019
Graduate Computer Architecture, handouts, by Prof. Asanovic, University of California at Berkeley, Spring 2018.

## Slide 6: What is Computer Architecture?
Application
In its broadest definition, computer architecture is the design of
the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies.
Gap too large to bridge
in one step
(but there are exceptions, e.g. magnetic compass)
Physics

## Slide 7: Abstraction Layers in Modern Systems
Application
Algorithm Programming Language
Operating System/Virtual Machines Instruction Set Architecture (ISA) Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Devices Physics

## Slide 8: Architecture continually changing
Cost of software development makes compatibility a major force in market
Applications
Technology
Applications
suggest how to improve technology, provide revenue to fund development
Improved technologies make new applications possible

## Slide 9: Major Technology Generations
[from Kurzweil]
Bipolar
CMOS
nMOS
pMOS
Vacuu m Tubes
Relays
Electromechanical
?

## Slide 10: Single-Thread Processor Performance

## Slide 11: Upheaval in Computer Design
Most of last 50 years, Moore’s Law ruled
  Technology scaling allowed continual performance/energy improvements without changing software model
Last decade, technology scaling slowed/stopped
  Dennard (voltage) scaling over (supply voltage ~fixed)
  Moore’s Law (cost/transistor) over?
  No competitive replacement for CMOS anytime soon
  Energy efficiency constrains everything
No “free lunch” for software developers, must consider:
  Parallel systems
  Heterogeneous systems

## Slide 12: Today’s Dominant Target Systems
Mobile (smartphone/tablet)
  >1 billion sold/year
  Market dominated by ARM-ISA-compatible general-purpose processor in system-on-a-chip (SoC)
  Plus sea of custom accelerators (radio, image, video, graphics, audio, motion, location, security, etc.)
Warehouse-Scale Computers (WSCs)
  100,000’s cores per warehouse
  Market dominated by x86-compatible server chips
  Dedicated apps, plus cloud hosting of virtual machines
  Now seeing increasing use of GPUs, FPGAs, custom hardware to accelerate
workloads
Embedded computing
  Wired/wireless network infrastructure, printers
  Consumer TV/Music/Games/Automotive/Camera/MP3
  Internet of Things!

## Slide 13: Computer Architecture: A Little History
Why worry about old ideas?
Those who ignore history are doomed to repeat it
Helps to illustrate the design process, and explains why certain decisions were taken
Because future technologies might be as constrained as older ones

## Slide 14: Changing Face of Computing
1960s: mainframes
1970s: mini-computers
1980s: Desktop computers
  Desktop
  Workstation
  → Servers
    Reliable
    Long term file storage and access
    Larger memory
    More computing power
1990s: Embedded, Internet
  PDA
  Set top boxes, Game consoles
2000s:
  ? (multi-core, networked, ..)
  Personal Mobile Devices
  Clusters / Cloud
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran
14

## Slide 15: Analog Computers
Analog computer represents problem variables as some physical quantity (e.g., mechanical displacement, voltage on a capacitor) and uses scaled physical behavior to calculate results
[Marsyas, Creative Commons BY-SA 3.0]
Antikythera mechanism c.100BC
[BenFrantzDale, Creative Commons BY-SA 3.0]
Wingtip vortices of Cessna tail in wind tunnel

## Slide 16: Digital Computers
Represent problem variables as numbers encoded using discrete steps
  Discrete steps provide noise immunity
Enables accurate and deterministic calculations
  Same inputs give same outputs exactly
Not constrained by physically realizable functions

## Slide 17: IBM 701 (1952)
IBM’s first commercial scientific computer
Main memory was 72 William’s Tubes, each 1Kib, for total of 2048 words of 36 bits each
– Memory cycle time of 12µs
Accumulator ISA with multipler/quotient register
18-bit/36-bit numbers in sign-magnitude fixed-point
Misquote from Thomas Watson Sr/Jr:
“I think there is a world market for maybe five computers”
Actually TWJr said at shareholder meeting:
“as a result of our trip [selling the 701], on which we expected to get orders for five machines, we came home with orders for 18.”

## Slide 18: IBM 650 (1953)
The first mass-produced computer
Low-end system with drum-based storage and digit serial ALU
Almost 2,000 produced

## Slide 19
IBM 360 : A General-Purpose Register (GPR) Machine
Processor State
  16 General-Purpose 32-bit Registers
    may be used as index and base register
    Register 0 has some special properties
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW)
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
  But no instruction contains a 24-bit address!
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words
The IBM 360 is why bytes are 8-bits long today!

## Slide 20: IBM Mainframes survive until today
Advanced Computer Architecture-Fall 2020, AUT, Tehran, Iran 34
© 2017 IBM Corporation
10 cores per CP-chip
5.2GHz
Cache Improvements:
  128KB I$ + 128KB D$
  2x larger L2 D$ (4MB)
  2x larger L3 Cache
  symbol ECC
New translation & TLB design
  Logical-tagged L1 directory
  Pipelined 2nd level TLB
  Multiple translation engines
Pipeline Optimizations
  Improved instruction delivery
  Faster branch wakeup
  Improved store hazard avoidance
  2x double-precision FPU bandwidth
  Optimized 2nd generation SMT2
Better Branch Prediction
  33% Larger BTB1 & BTB2
  New Perceptron & Simple Call/Return Predictor
z14 processor design summary
Micro-Architecture Architecture
PauseLess Garbage Collection
Vector Single & Quad precision
Long-multiply support (RSA, ECC)
Register-to-register BCD arithmetic
Accelerators
Redesigned in-core crypto-accelerator
  Improved performance
  New functions (GCM, TRNG, SHA3)
Optimized in-core compression accelerator
  Improved start/stop latency
  Huffman encoding for better compression ratio
  Order-preserving compression