## Slide 1: FPGA Technology Mapping Algorithms
ABC

## Slide 2: ABC LUT Mapping
F(a,b,c,d) = ab + d(ac’+bc)
F(a,b,c,d) = ac’(b’d’)’ + c(a’d’)’ = ac’(b+d) + bc(a+d)
6 nodes
4 levels
7 nodes
3 levels
b
c
a
c
a
b
d
a
c
b
d
b
c
a
d
VTR (Verilog to Routing):
  AIG (And-Inverter Graph)
    Boolean network composed of two-input ANDs and inverters
2-input AND
NOT

## Slide 3: Structural Cuts in AIG
Cut of a node n:
  A set of nodes in transitive fan-in such that
    every path from the node to PIs is blocked by nodes in the cut.
k-feasible cut:
  size of the cut ≤ k
a
b
c
p
q
n
{p, b, c}: 3-feasible cut of node n (also a 4-feasible cut)
k-feasible cut can be replaced by a k-LUT.

## Slide 4: Cut Enumeration
a
b
c
d
f
e
Dotted lines: NOT
Different cuts for the same node
The mapped netlist
a
b
c
d
e
f

## Slide 5: Cut Enumeration
  For each node, tries all possible cuts.
  Finds the best.
  Nodes processed in topological order (from inputs)

## Slide 6: Cut Computation
a
b
c
p
q
{ {p}, {a, b} }
{ {q}, {b, c} }
{ {a} }
{ {b} }
{ {c} }
n
{ {n}, {p, q}, {p, b, c}, {a, b, q}, {a, b, c} }
Computation is done bottom-up
  Set of cuts of a node: ‘cross product’ of the sets of cuts of its children
  Any cut that is of size greater than k is discarded.
  Best cut (area, delay, power) is selected.

## Slide 7: Later Problems/Issues
Area optimization while maintaining performance
  DAOmap [Chen04] guarantees optimal delay, reducing area significantly
Integrated approaches:
  with retiming
  with synthesis
  with clustering and placement
More area/delay reduction heuristics
  Improvements on delay and area as well as the runtime and memory requirements
Power minimization techniques [Cheng07]
  TM for dual supply voltages
TM for reliability
Parallel algorithms for TM
Notes: dp9D_2.ppt:
Power Minimization
PowerMinMap, [Li, et al, ASPDAC’03]
Emap, [Lamoureux, et al, ICCAD’03]
DVmap, [Chen, et al, FPGA’04]

## Slide 8: Later Problems/Issues
Mapping for FPGAs with heterogeneous resources:
  FPGAs with different LUT sizes
    Stratix-5:
    Virtex-7:
  FLUT (Fracturable LUT) Mapping [Dickin11]
Mapping with embedded memory blocks (not so recent):
  Unused EMBs can be used to implement logic.
    Large multi-input/multi-output LUTs
Mapping DSP blocks [Smith24]
Notes: dp9D_2.ppt:
Power Minimization
PowerMinMap, [Li, et al, ASPDAC’03]
Emap, [Lamoureux, et al, ICCAD’03]
DVmap, [Chen, et al, FPGA’04]

## Slide 9: SliceM

## Slide 10: SliceM
LUT:
  Can implement one 6-input function
    Only O6 can be used
  Can implement two 5-inout functions with common inputs (A1-A5)
    O5 and O6 are used

## Slide 11: Altera Stratix Logic Element

## Slide 12: Adaptive Logic Module
ALM:
  An 8-input structure that can implement many combinations of logic functions, including:
    One 6-input logic function
    Two 4-input logic functions
    One 5-input and one 3-input function
    Two 6-input functions that share the same logic function and 4 inputs

## Slide 13: Optimality Study of TM Algorithms

## Slide 14: Potential Success of TM Algorithms
Area-optimal LUT mapping is NP-complete.
Optimality study of LUT-based TM [Cong06]:
  LEKO examples:
    Logic synthesis Examples with Known Optimal
    No optimization done
    Existing academic LUT-mapping algorithms and commercial tools:
      Gap: 5% to 23% (average 15%):
      Quartus: 5% (Commercial) (does logic optimization too)
      DAOmap: 23% (Academic)

## Slide 15: LEKO Construction
  Constructing a network Gn of an arbitrarily large size that has a known optimal technology mapping solution.
    n inputs and outputs
  G is constructed in a special way by replicating a small circuit with a known optimal mapping solution into a circuit of any size that also has a known optimal mapping solution.
  The building block of our construction is a “hard graph” named G5, with the following properties:
    1. It has five inputs and five outputs.
    2. Every output is a function of all five inputs.
    3. Each internal node of G5 has exactly two inputs.
    4. There exists an optimal (in terms of area/depth) mapping of G5 into a 4-LUT mapping solution, denoted M5, such that M5 only has 4-LUTs (no 3-LUTs or 2-LUTs).

## Slide 16: Potential Success of TM Algorithms
  LEKU examples:
    Logic synthesis Examples with Known Upper bounds (on area)
    LEKUs require logic restructuring/optimization to achieve the optimal mapping solutions.
    Average optimality gap: from x70 to x504 over known upper bounds (average: x172)
   Poor performance of logic optimization + technology mapping algorithms

## Slide 17: References
  [Mishchenko] A. Mishchenko, Introduction to Logic Synthesis with ABC.ppt.
  [Brayton] R. Brayton, and A. Mishchenko, “ABC: An Academic Industrial-Strength Verification Tool. In: T. Touili, B. Cook, P. Jackson, (eds) Computer Aided Verification. CAV 2010. Lecture Notes in Computer Science, vol 6174. Springer, Berlin, Heidelberg.
  VPR 5.0, http://www.eecg.utoronto.ca/vpr.
  VPR 6.0, Beta Release, May 30, 2011
  Now: VTR 8, March 2020.
    Murray, et al. "VTR 8: High Performance CAD and Customizable FPGA Architecture Modelling". ACM Transactions on Reconfigurable Technology and Systems, Vol. 13, No. 2, 2020, pp. 1-55.

## Slide 18: References
  [Chen04] Chen, Deming, and Jason Cong. "DAOmap: A depth-optimal area optimization mapping algorithm for FPGA designs." In IEEE/ACM International Conference on Computer Aided Design, ICCAD, pp. 752-759, 2004.
  [Smith24] Smith, et al. "FPGA Technology Mapping Using Sketch-Guided Program Synthesis." In Proceedings of the 29th ACM International Conference on Architectural Support for Programming Languages and Operating Systems, pp. 416-432. 2024.