## Slide 1: Advanced Computer Architecture System-on-Chip
By Amirreza Hosseini
Dr. Farbeh

## Slide 2: SOC architecture and design
system-on-chip (SOC)
  processors: become components in a system
SOC covers many topics
  processors, cache, memory, interconnect, design tools
need to know
  user view: variety of processors
  basic information: technology and tools
  processor internals: effect on performance
  storage: cache, embedded and external memory
  interconnect: buses, network-on-chip
  evaluation: processor, cache, memory, interconnect
  advanced: specialized processors, reconfiguration
  design productivity: system modelling, design exploration

## Slide 3: System on a Chip: driven by semiconductor advances

## Slide 4: Basic system-on-chip model

## Slide 5: SOC vs processors on chip
with lots of transistors, designs move in 2 ways:
  complete system on a chip
  multi-core processors with lots of cache
 | System on chip | Processors on chip
processor | multiple, simple, heterogeneous | few, complex, homogeneous
cache | one level, small | 2-3 levels, extensive
memory | embedded, on chip | very large, off chip
functionality | special purpose | general purpose
interconnect | wide, high bandwidth | often through cache
power, cost | both low | both high
operation | largely stand-alone | need other chips

## Slide 6: iPhone: has System-on-Chip

## Slide 7: iPhone SOC
7
1 GHz ARM Cortex A8
I/O
I/O
I/O
Processor
Memory

## Slide 8: AMD’s Barcelona Multicore Processor
4 out-of-order cores
1.9 GHz clock rate
65nm technology
3 levels of caches
integrated Northbridge
Core 1
Core 2
Core 3
Core 4
Northbridge
512KB L2
512KB L2
512KB L2
512KB L2
2MB shared L3 Cache
http://www.techwarelabs.com/reviews/processors/barcelona/

## Slide 9: Why System on Chip
http://www.c-p-e.be/cypros/
802.11
LAN
Radio
Video camera
LCD, TFT display
GPS
Keypad
Camera
Compact Flash

## Slide 10: System of Chip Components
Analog
Digital
Memory
Software/ OS
http://low-powerdesign.com/cadence_karnane.htm
Set top box

## Slide 11: SoC Hardware Architecture
Often used in embedded application.
How to implement an application on a HW platform executing some SW programs?
source: wiki

## Slide 12: SOC design: key ideas
to design and evaluate an SOC, designers need to understand:
  its components: processors, memory, interconnect
  applications that it targets
SOC economics heavily dependent on:
  costs: initial design, marginal production
  volume: applicability, lifetime
reducing design complexity
  Intellectual Property (IP)
  reconfigurable technology

## Slide 13: SOC processors
usually a mix of special and general purpose (GP)
  can be proprietary design or purchased IP
commonly GP processor is purchased IP
  includes OS and compiler support
GP processor optimized for an application
  additional instructions
  vector units

## Slide 15: Research
Interconnect topologies
  e.g. bus
Hybrid modules, Analog, Digital, ASIP, i.e. integration of mixed signal elements.
On chip communication, power, switching delay, performance such as throughput.
Hardware software co design for reuse.
Mixed Signal (integrated analog blocks such as A to D and D to A converters, phase-locked loops, and adaptive filters.)

## Slide 16: Traditional architecture
Current NOC (arteris.com)

## Slide 17: Interconnect topologies
Bus
Star
Cube
Tree
Spin

## Slide 18: Some processors for SOCs
SOC | Basic ISA | Processor description
Freescale c600: signal processing | PowerPC | Superscalar with vector extension
ClearSpeed CSX600: general | Proprietary | Array processor with 96 processing elements
PlayStation 2: gaming | MIPS | Pipelined with 2 vector coprocessors
ARM VFP11: general | ARM | Configurable vector coprocessor

## Slide 19: Processor types: overview
Processor type | Architecture / Implementation approach
SIMD | Single instruction applied to multiple functional units
Vector | Single instruction applied to multiple pipelined registers
VLIW | Multiple instructions issued each cycle under compiler control
Superscalar | Multiple instructions issued each cycle under hardware control

## Slide 20: Adding instructions
additional instructions to support specialized resources
  exception: superscalar, with hardware control
instructions can be added to base processor for coprocessor control
  VLIW: Very Large Instruction Word
  Array
  Vector

## Slide 21: Sequential and parallel machines
basic single stream processors
  pipelined: basic sequential
  superscalar: transparently concurrent
  VLIW: compiler generated concurrency
multiple stream
  array processors
  vector processors
multiprocessors

## Slide 22: Sequential processors
operation
  generally transparent to sequential programmer
  appear as in order instruction execution
pipeline processor
  execution in order
  limited to one instruction execution / cycle
superscalar processor
  multi instructions / cycle, managed by hardware
VLIW
  multi op execution / cycle, managed by compiler

## Slide 23: PCI serial and parallel
http://computer.howstuffworks.com/pci-express1.htm

## Slide 24: System Chip – Advantages and Issues
Advantages
  Easily reprogrammable, reuse of Intellectual property.
  Lower chip area, reduce in silicon
  Low cost
Issues
  On chip routing and timing.
  Limitations of On chip resources

## Slide 25: Parallel processors
execution managed by programmer
array processors
  single instruction stream, multiple data streams: SIMD
vector processors
  SIMD
multiprocessors
  multiple instruction streams, multiple data streams: MIMD

## Slide 26: Memory and addressing
many SOC memory designs use simple embedded memory
  a single level cache
  real (rather than virtual) addressing
as SOC become more complex
  their designs are expected to use more complex memory and addressing configurations

## Slide 27
Three levels of
addressing

## Slide 28: User view of memory: addressing
a program: process address (offset + base + index)
  virtual address: process address + process id
a process: assigned a segment base and bound
  system address: segment base + process address
pages: active localities in main/real memory
  virtual address: translated by table lookup to real address
  page miss: virtual pages not in page table
TLB (translation look-aside buffer): recent translations
  TLB entry: corresponding real and (virtual, id) address
a few hashed virtual address bits address TLB entries
  if virtual, id = TLB (virtual, id) then use translation

## Slide 29
The TLB and
The MMU

## Slide 30: SOC interconnect
interconnecting multiple active agents requires
  bandwidth: capacity to transmit information (bps)
  protocol: logic for non-interfering message transmission
bus
  AMBA (adv. Microcontroller bus architecture) from ARM, widely used for SOC
  bus performance: can determine system performance
network on chip
  array of switches
  statically switched: eg mesh
  dynamically switched: eg crossbar

## Slide 31: Bus based SOC

## Slide 32: Network on a Chip

## Slide 33: Networks-on-Chip (NoCs)

## Slide 34: Motivation
Bus has been the most popular interconnect for multiprocessor systems
When scaling feature sizes and frequency, wire delays remain larger than clock cycle
Need for interconnect with deterministic delays and scalability
When expanding to a many core-system, contention decreases throughput

## Slide 35: What is a Network-on-Chip (NoC)?
  Leveraging existing computer networking principles to improve inter-component intra-chip communications
  Each on-chip component connected by an intelligent switch to particular communication wire(s)
  Improvement over standard bus based interconnections for SoC architectures in terms of throughput

## Slide 37: Topologies
CLICHÉ Torus Folded torus

## Slide 38: Topologies contd.
SPIN Octagon BFT

## Slide 40: Switching
  Circuit Switching
  Dedicated path, or circuit, is established over which data packets will travel
  Naturally lends itself to time-sensitive guaranteed service due to resource allocation
  Reservation of bandwidth decreases overall throughput and increases average delays
  Packet Switching
  Intermediate routers are now responsible for the routing of individual packets through the network, rather than following a single path
  Provides for so-called best-effort services
  Sharing of resources allows for higher throughput

## Slide 41: Circuit Switching Example
Significant latency overhead prior to data transfer
Other requests forced to wait for resources
Acknowledgement
Configuration Probe
Data
Circuit
0
5

## Slide 42: Store & Forward Switching
Source node
Intermediate nodes
Destination node
Each node along a route waits until a packet is completely received (stored) and then the packet is forwarded to the next node
Two resources are needed
  Packet-sized buffer in the switch
  Exclusive use of the outgoing channel

## Slide 43: Store & Forward Switching
S&F switching forwards a packet only when there is enough space available in the receiving buffer to hold the entire packet.
Thus, there is no need for dividing a packet into flits. This reduces the overhead, as it does not require circuits such as a flit builder, a flit decoder, a flit stripper and a flit sequencer.
Nevertheless, such a switching technique requires a large amount of buffer space at each node. Thus, it may not be a feasible solution for embedded applications

## Slide 44: Store & Forward Switching Example
High per-hop latency
Larger buffering required

## Slide 45: Store & Forward Switching
Finer grained sharing of the link bandwidth
Routing, arbitration, switching overheads experienced for each packet
Increased storage requirements at the nodes
Packetization and in-order delivery requirements
Alternative buffering schemes
  Use of local processor memory
  Central (to the switch) queues

## Slide 46: Switching contd.
  Wormhole Switching
  Message is divided up into smaller, fixed length flow units called flits
  Only first flit contains routing information, subsequent flits follow
  Buffer size is significantly reduced due to the limitation on the number of flits needed to be buffered at any given time
  Virtual Channels
  Allows for several instances of wormhole switching
  Additional buffers are added, which increases overall switch size, but significantly increases throughput

## Slide 47: Performance Metrics
Simulator developed to measure:
Throughput (in flits)
Latency (of flits)
Energy (per packet)
Hardware model developed to estimate:
Area (router and link overhead)

## Slide 48
Network Interface
Router
Router
Core
NI
Memory
NI
Transmitter side
Notes: 48
48

## Slide 49
Core
Router
NI
FT
D
S
P#
PS
stw r9, 0(r10)
Network Interface
Notes: 49
49

## Slide 50: SOC design approach
understand application (compiler, OS, memory and real time constrains)
select initial die area, power, performance targets; select initial processors, memory, interconnect
assume target processor and interconnect performance, design and evaluate memory
evaluate and redesign processors with memory
design interconnect to support processors and memory
repeat and iterate to optimize

## Slide 51: SOC design approach

## Slide 52: Processor optimization example
given embedded ARM processor
  in an SOC chip
1 IALU vs 2 IALU vs 3 IALU vs 4 IALU
  instructions per cycle?
16k L1 instruction cache vs 32k L1 i-cache
  how much improvement? less power?
branch predictor: taken vs not-taken
  misprediction rate?
aim: explore this large design space

## Slide 53: Design cost: product economics
increasingly product cost determined by
  design costs, including verification
  not marginal cost to produce
manage complexity in die technology by
  engineering effort
  engineering cleverness

## Slide 54: Design complexity

## Slide 55: Cost: product program vs engineering

## Slide 56: Product volume dictates design effort

## Slide 57: Summary
to design and evaluate an SOC, designers need to understand:
  its components: processors, memory, interconnect
  applications that it targets
SOC economics heavily dependent on:
  costs: initial design, marginal production
  volume: applicability, lifetime
reducing design complexity
  Intellectual Property (IP)
  reconfigurable technology

## Slide 58
Akram Ben Ahmed, Shohei Miura, A. Ben Abdallah, Run-Time Monitoring Mechanism for Efficient Design of Network-on-Chip Architectures, to appear in the 6th International Workshop on Engineering Parallel and Multicore Systems (ePaMuS2013'), July 2013.
Akram Ben Ahmed, A. Ben Abdallah, Low-overhead Routing Algorithm for 3D Network-on-Chip, IEEE Proc. of the The Third International Conference on Networking and Computing (ICNC'12), pp. 23-32, 2012.
Akram Ben Ahmed, A. Ben Abdallah, LA-XYZ: Low Latency, High Throughput Look-Ahead Routing Algorithm for 3D Network-on-Chip (3D-NoC) Architecture, IEEE Proceedings of the 6th International Symposium on Embedded Multicore SoCs (MCSoC-12), pp. 167-174, 2012.
Akram Ben Ahmed, A. Ben Abdallah, ONoC-SPL Customized Network-on-Chip (NoC) Architecture and Prototyping for Data-intensive Computation Applications, IEEE Proceedings of The 4th International Conference on Awareness Science and Technology, pp. 257-262, 2012.
A. Ben Ahmed, A. Ben Abdallah, Efficient Look-Ahead Routing Algorithm for 3D Network-on-Chip (3D-NoC),IEEE Proceedings of the 6th International Symposium on Embedded Multicore SoCs (MCSoC-12,) pp. 167-174,2012.
R. Okada, Architecture and Design of Core Network Interface for Distributed Routing in OASIS NoC, Technical Report, ASL- Parallel Architecture Group, School of Computer Science and Engineering, The University of Aizu, March 2012.
A. Ben Ahmed, A. Ben Abdallah, K. Kuroda,Architecture and Design of Efficient 3D Network-on-Chip (3D NoC) for Custom Multicore SoC, IEEE Proc. of the 5th International Conference on Broadband, Wireless Computing, Communication and Applications (BWCCA-2010), pp.67-73, Nov. 2010. (best paper award) (slides)
K. Mori, A. Esch, A. Ben Abdallah, K. Kuroda, Advanced Design Issues for OASIS Network-on-Chip Architecture, IEEE Proc. of the 5th International Conference on Broadband, Wireless Computing, Communication and Applications (BWCCA-2010),pp.74-79, Nov. 2010. slides
T. Uesaka, OASIS NoC Topology Optimization with Short-Path Link, Technical Report, Systems Architecture Group,March 2011
K. Mori, A. Ben Abdallah, OASIS NoC Architecture Design in Verilog HDL, Technical Report,TR-062010-OASIS, Adaptive Systems Laboratory, the University of Aizu, June 2010. slides
Shohei Miura, Abderazek Ben Abdallah, Kenichi Kuroda, PNoC: Design and Preliminary Evaluation of a Parameterizable NoC for MCSoC Generation and Design Space Exploration, The 19th Intelligent System Symposium (FAN 2009), pp.314-317, Sep.2009.
Kenichi Mori, Abderazek Ben Abdallah, Kenichi Kuroda, Design and Evaluation of a Complexity Effective Network-on-Chip Architecture on FPGA, The 19th Intelligent System Symposium (FAN 2009), pp.318-321, Sep. 2009.
A. Ben Abdallah, T. Yoshinaga and M. Sowa, "Mathematical Model for Multiobjective Synthesis of NoC Architectures", IEEE Proc. of the 36th International Conference on Parallel Processing, Sept. 4-8, 2007.
A. Ben Abdallah, Masahiro Sowa, "Basic Network-on-Chip Interconnection for Future Gigascale MCSoCs Applications: Communication and Computation Orthogonalization", JASSST2006, Dec. 4-9th, 2006.
Book: Multicore Systems-on-Chip: Practical Hardware/Software Design, 2nd Edition, Author: A. Ben Abdallah, Publisher: Springer, (2013) , ISBN-13: 978-9491216916. [Amazon]
References