## Slide 1: Memory Technologies Spring 2024
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Reference (for this lecture)
Design Exploration of Emerging Nano-scale Non-volatile Memory, Hao Yu and Yuhao Wang, Springer, 2014
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 3: Nanoscale Nonvolatile Memories
SRAM
  Fastest memory
  Significant leakage power
  Limited capacity (few megabyte)
DRAM
  Fastest after SRAM
  Large refresh power in large capacity
Flash
  No leakage power
  Slow
  Limited endurance
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 4: Nanoscale Nonvolatile Memories
Memory Hierarchy
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 5: Nanoscale Nonvolatile Memories
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 6: Resistive Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 7: Resistive Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Memristor
  Predicted in 1976 by Leon Chua
  Discovered 30 years later in HP Labs
  Its resistance is determined by the current passed through in the past as if it can remember its history
  When current flows in one direction, its electrical resistance increases
  When current flows in the opposite direction, resistance decreases
  When the current is stopped, retains its previous resistance

## Slide 8: Memristor
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Bistable states
  High resistance
  Low resistance
  Write operation
    Applying large current: changes its resistance rapidly
  Read operation
    small current is applied to detect its resistance without significantly changing its resistance
  First physical realization
    2008: HP Labs

## Slide 9: Conductive Bridging Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
CBRAM OR programmable metalization cell (PMC)
  Two-terminal cylinder-shaped nanoscale device
  Each CBRAM memory cell
    two metal electrodes
      One relatively inert (e.g., tungsten)
      One electrochemically active (e.g., silver or copper)
      A solid electrolyte between them
    Within the solid electrolyte, there exists a vertical conductive filament that grows from the inert electrode

## Slide 10: Conductive Bridging Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
CBRAM OR programmable metalization cell (PMC)
  Filament vertically growth by active voltage
    Electrode bridge together
    Low-resistance or ON-state
  Filament vertically shrinks by negative voltage
    High-resistance or OFF-state

## Slide 11: Magnetoresistive Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Giant magnetoresistance (GMR): 1988
  Groups of Albert Fert of the University of Paris-Sud, France
  Peter Grünberg of Forschungszentrum Jülich, Germany
GMR Effect
  A significant change in the electrical resistance
    Depending on the magnetization of adjacent ferromagnetic layers

## Slide 12: Magnetoresistive Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
MRAM: Magnetoresistive random-access memory (MRAM)
Toggle mode MRAM
  First generation of the MRAM
  External magnetic field is needed
  Current-induced magnetic field:
    To be compatible with the electronic system

## Slide 13: Magnetoresistive RAM
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Spin-Transfer Torque MRAM (STT-MRAM)
  Based on
    Spin-polarized current-induced MTJ switching
    spin-transfer torque effect
  Fast, lower power consumption, better scalability
  Spin-transfer phenomena
    Spin polarized current

## Slide 14: Racetrack Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Racetrack or Domain Wall
  A thin ferromagnetic film strip
    Consists of many magnetic domains
  Train-like domains can be pushed to move bidirectionally synchronously

## Slide 15: Racetrack Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Racetrack or Domain Wall
  Access time?
  RAM?!
  Density?

## Slide 16: Phase-Change RAM
Memory Technologies, Spring 2024, AUT, Tehran, Iran
PCM
  Phase changing technology of chalcogenide materials such as Ge2SbTe5 (GST)
  Two different stable states
    Crystalline
    Amorphous

## Slide 17: Phase-Change RAM
Memory Technologies, Spring 2024, AUT, Tehran, Iran
The chalcogenide crystal structure can be thermally switched between the two states

## Slide 18: Ferroelectric Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
FeRAM
  Ferroelectric capacitor
    Ferroelectric instead of dielectric material
  Ferroelectric capacitors characteristics
    Have two stable states
    Retain their states without electrical power

## Slide 19: Ferroelectric Random-Access Memory
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Bistable states
  Polarization states of the ferroelectric material
    Positive
    Negative
Write operation
  ±VDD is applied across the ferroelectric capacitor
Read operation
  Float BL
  Distructive

## Slide 20: FeRAM
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Pros
  No leakage and refresh power
  Unlimited write-erase cycle (1015)
  Faster than flash
  Symmetric read/write
Cons
  Density and scaling
  Manufacturing difficulties

## Slide 21: Conclusion
Memory Technologies, Spring 2024, AUT, Tehran, Iran