## Slide 1: Memory Technologies Spring 2024
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Reference (for this lecture)
Memory Systems: Cache, DRAM, Disk, Bruce Jacob, Spencer W. Ng, and David T. Wang, Morgan Kaufmann, 2008
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 3: Memory Subsystem
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Richard Sites, 1996
  “Across the industry, today’s chips are largely able to execute code faster than we can feed them with instructions and data. There are no longer performance bottlenecks in the floating-point multiplier or in having only a single integer unit. The real design action is in memory subsystems—caches, buses, bandwidth, and latency. … . Increasing the width of instruction issue and increasing the number of simultaneous instruction streams only makes the memory bottleneck worse. … . I expect that over the coming decade memory subsystems design will be the only important design issue for microprocessors. ”

## Slide 4: Memory Subsystem
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Flat memory system
  Attractive for simplicity
Memory hierarchy
  Performance of the fastest component
  Cost per bit of the cheapest component
  Energy consumption of the most energy-efficient component
The use of a hierarchy allowed designers to treat system design as a modularized process

## Slide 5: Memory Hierarchy
Memory Technologies, Spring 2024, AUT, Tehran, Iran
A set of disparate subsystems that interact only through well-defined functional interfaces and that can be optimized in isolation
  No longer suffices for the design of modern memory systems
Many of the underlying implementation issues are becoming significant
  Physics of device and interconnect scaling
  The choice of signaling protocols and topologies to ensure signal integrity
  Design parameters such as granularity of access and support for concurrency
  Communication-related issues such as scheduling algorithms and queueing

## Slide 6: Memory Hierarchy
Memory Technologies, Spring 2024, AUT, Tehran, Iran
The real loss of performance is not seen in the CPU or caches or DRAM devices or disk assemblies themselves
  But, in the subtle interactions between these subsystems and in the manner in which these subsystems are connected
It has now become the case that a memory-systems designer, wishing to build a properly behaved memory hierarchy, must be intimately familiar with issues involved at all levels of an implementation, from cache to DRAM to disk

## Slide 7: Memory Systems
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Von Neumann model
  Code and data are essentially the same and reside in the same place
  All requests, whether for instructions or for data, go to this random-access memory.
The memory system must be able to handle randomly addressed requests
  In a manner that favors no particular request
Modern software is written to expect gigabytes of storage for data and
  Modern consumer expects this storage to be cheap
How many memory technologies provide both tremendous speed and tremendous storage capacity at a low price?

## Slide 8: Memory System
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Modern memory systems often have a terabyte of storage on the desktop and
  Provide instruction-fetch and data-access bandwidths of 128 GB/s or more
Nearly all of the storage in the system is non-volatile
Speculative execution on the part of the microprocessor is supported
All of this can be found in a memory system that has an average cost of
  roughly 1/100,000,000 pennies per bit of storage
The reason all of this is possible is because of locality of reference

## Slide 9: Locality of Reference
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Memory references tend to be localized in time and space
  Temporal locality: If you use something once, you are likely to use it again
  Spatial locality: If you use something once, you are likely to use its neighbor
A program does not need all of its data immediately accessible
A two level storage
  First level: provides immediate access to a subset of the program’s data
  Second level: holds the remainder of the data: slower and cheaper
  An appropriate heuristic: to manage the movement of data back and forth between the levels
Memory hierarchy: multiple levels of storage, each optimized for its assigned task

## Slide 10: Current Mem. Hierarchy
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Cache (SRAM)
  Very low latency (0.25 ns)
  Very high bandwidth (16-byte instruction/data block: 128 GB/s)
DRAM
  Relatively large
  Relatively fast
  Relatively cheap
  Fast enough and cheap enough
Disk
  Permanent storage
  Ultra-low cost per bit (less than 50¢ per gigabyte)

## Slide 11: Important Figures of Merit
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Performance
Energy consumption
Power dissipation
Predictability of behavior (i.e., real time)
Manufacturing costs
Reliability

## Slide 12: Performance
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Cycles per Instruction (CPI)
Memory-system CPI overhead
= Real CPI – CPI assuming perfect memory
Memory Cycles per Instruction (MCPI)
Cache miss rate

## Slide 13: Performance
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Average access time
= (hit rate.average to service hit) + (miss rate.average to service miss)
Million Instructions per Second (MIPS)
Comparing Performance
  The amount of time saved by using one design over another

## Slide 14: Energy Consumption/Power Dissipation
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Energy consumption is related to work accomplished
Power dissipation: the rate of consumption
Active (Dynamic) power
  Due to switching activity
Static power
  Due primarily to subthreshold leakage

## Slide 15: Energy Consumption/Power Dissipation
Memory Technologies, Spring 2024, AUT, Tehran, Iran
With each generation in process technology
  Active power
    Is decreasing on a device level
    Remains roughly constant on a chip level
  Leakage power
    Used to be insignificant relative to switching power
    Increases as devices become smaller
Energy consumption

## Slide 16: Energy Consumption/Power Dissipation
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Power-Delay Product
Energy-Delay Product
MIPS per watt

## Slide 17: Predictable (Real-Time) Behavior
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Popular figures of merit for predictability
  Worst-Case Execution Time (WCET): The longest amount of time a function could take to execute
  Response time: the time between a stimulus to the system and the system’s response (e.g., time to respond to an external interrupt)
  Jitter: the amount of deviation from an average timing value
Question
  Which one is predictable:
    Register file
    Caches
    On-chip RAM
    Main memory
    HDD

## Slide 18: Design (and Fabrication and Test) Costs
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Cost can be represented in many different ways
By “cost” we mean the cost of producing an item
  Design
  Test
  Manufacture
  Test
Popular figures of merit for cost
  Dollar cost (best, but often hard to even approximate)
  Design size, e.g., die area (cost of manufacturing a VLSI design is proportional to its area cubed or more)
  Packaging costs, e.g., pin count
  Design complexity (number of logic gates and/or transistors, lines of code, time to compile or synthesize, time to verify or run DRC (design-rule check), and many others, including a design’s impact on clock cycle time

## Slide 19: Design (and Fabrication and Test) Costs
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Relative cost
  Allowing differing technologies or approaches to be placed on equal footing for a comparison
Cost per storage bit/byte/KB/MB/etc.
  allows cost comparison between different storage technologies
Die area per storage bit
  Allows size efficiency comparison within same process technology

## Slide 20: Reliability
Memory Technologies, Spring 2024, AUT, Tehran, Iran
“Reliability” means many things to many different people
Reliability is achieved by redundancy
We mean reliability of the data stored within the memory system
  How easily is our stored data corrupted or lost
  How can it be protected from corruption or loss

## Slide 21: Reliability
Memory Technologies, Spring 2024, AUT, Tehran, Iran
Popular figures of merit for measuring reliability
  Mean Time Between Failures (MTBF): given in time (seconds, hours, etc.) or number of uses
  Bit-error tolerance: how many bit errors in a data word or packet the mechanism can correct, and how many it can detect (but not necessarily correct)
  Error-rate tolerance: how many errors per second in a data stream the mechanism can correct
  Application-specific metrics: how much radiation a design can tolerate before failure, etc.