## Slide 1: Memory Technologies Spring 2024
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2
Reference
  Memory Systems: Cache, DRAM, Disk, Bruce Jacob, Spencer W. Ng, and David T. Wang, Morgan Kaufmann, 2008
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 3: Cache Principles
Caches are transparent memories
  They work independently of the client making the request
  Have built-in heuristics that determine what data to retain
Caches that are explicitly managed by the client making the request are called: scratch-pads or scratchpad memories (SPMs)
Locality Principles
  Temporal Locality
  Spatial Locality
  Anything else?
Algorithmic Locality
  When a program repeatedly accesses data items or executes code blocks that are distributed widely across the memory space
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 4: Logical Organization Basics
Blocks, sets, tags
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 5: Content Management
To Cache or Not to Cache
  determine which references are the best candidates for caching and to ensure that their corresponding data values are in the cache at the time the application requests them
  must consider the currently cached items and decide which should be evicted to make room for more important data not yet cached
  Cache Replacement algorithms
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 6: Consistency Management
Keep the cache consistent with itself
  There should never be two copies of a single item in different places of the cache, unless it is guaranteed that they will always have the same value
Keep the cache consistent with the backing store
  The value kept in the backing store should be up-to-date with any changes made to the version stored in the cache
    Write-back and write-through policies
Keep the Cache Consistent with Other Caches
  Other caches in the system should all be treated much like the backing store in terms of keeping the various copies of a datum up-to-date
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 7: Inclusion and Exclusion
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 8: A Taxonomy of Cache Types
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 9: Virtual Addressing
The backing store for a processor cache is usually taken to be main memory: physically addressed
  Processor generate virtual addresses
  Should caches use the physical address to identify a cached item?
    Not necessarily
On each cache access, the cache is indexed, and the tags are compared
  Four choices for cache organization
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 10: Cache Addressing
Physically indexed, physically tagged
  The cache is indexed and tagged by its physical address
  the virtual address must be translated before the cache can be accessed
Pros
  since the cache uses the same namespace as physical memory, it can be entirely controlled by hardware, and the operating system need not concern itself with managing the cache.
Cons
  Address translation is in the critical path (TLB)
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 11: Cache Addressing
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 12: Cache Addressing
Physically indexed, virtually tagged
  The cache is indexed by its physical address, but the tag contains the virtual address
  If the physical address is available at the start of the procedure, then why not use the physical address as a tag?
  If a single physical page is being shared at two different virtual addresses, then there will be contention for the cache line
Pros
  The operating system need not perform explicit cache management
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 13: Cache Addressing
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 14: Cache Addressing
Virtually indexed, physically tagged
  The cache index is available immediately since it needs no translation, and the tag requires translation
  The translation of the virtual address can happen at the same time as the cache index
    Address translation is not in the critical path
Pros
  Much faster access time than a physically indexed cache
  Reduced need for management as compared to a virtually indexed, virtually tagged cache
    Hardware can ensure that multiple aliases to the same physical block do not reside in multiple entries of a set
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 15: Cache Addressing
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 16: Cache Addressing
Virtually indexed, virtually tagged
  The cache is indexed and tagged by the virtual address
Pros
  Address translation is not needed anywhere in the process
  A translation lookaside buffer is not needed
    If one is used, it only needs to be accessed when a requested datum is not in the cache
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 17: Cache Addressing
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 18: Implementation Issues
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 19: Read Operation
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 20: Address Decoding
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 21: Predecoding
Predecoding: using one level of logic to AND subsets of the address
Minimizing fan-in
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 22: Row and Column Decoding
Two-dimensional decoding
  A subset of the address accesses a single row of the array (the row address), and a separate subset is used to select a fraction of all of the columns accessed within the row
Non-Partitioned Decoding
  Number of connected cells to the row’s wordlines and the column’s bitlines
    Total capacitance and power dissipation
  physical lengthening of the SRAM array
    increasing the wordline wire length and its parasitic wiring capacitance
  More power in the bitlines is wasted during each access
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 23: Divided Wordline (DWL)
Dividing the memory array along the top-level wordline
  into a fixed number of blocks
Memory Technologies, Spring 2024, AUT, Tehran, Iran

## Slide 24: Divided Wordline (DWL)
Partitioning effect on power and delay
  8K x 8 SRAM
Memory Technologies, Spring 2024, AUT, Tehran, Iran