## Slide 1: Memory Technologies Spring 2024
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2
Reference
  Memory Systems: Cache, DRAM, Disk, Bruce Jacob, Spencer W. Ng, and David T. Wang, Morgan Kaufmann, 2008

## Slide 3: Overview of DRAMs

## Slide 4: DRAM Internals
DRAM memory array

## Slide 5: DRAM Internals
DRAM memory chip
  Each set of memory arrays that operates independently of other sets is referred to as a bank, not an array.

## Slide 6: DRAM Internals
DIMM, rank, bank

## Slide 7: Memory Bus Organization

## Slide 8: Memory Bus Organization
DRAM Access

## Slide 9: Evolution of the DRAM Architecture
Fast Page Mode (FPM)
  Allows the row to remain open across multiple CAS commands
  Eliminates the need for a row address if data is located in the row previously accessed
  Speeds up successive accesses to the same row of the DRAM core
Extended data out (EDO)
  Also referred to as Hyper Page Mode enabled DRAM
  Adds a few transistors to the output drivers of an FPM DRAM to create a latch between the sense amps and the output pins of the DRAM
  A new access cycle could be started while the data output from the previous cycle was still present
  It held the output valid until either
    RAS was dis-asserted, or
    a new CAS falling edge selected a different column address

## Slide 10: Evolution of the DRAM Architecture
Burst EDO DRAM
  Could process four memory addresses in one burst
  By adding an address counter on the chip to keep track of the next address
  Never reached the volume of production that EDO and SDRAM did
Synchronous DRAM
  Adding a clock (and a clock enable) line
    All other signals are received on the rising edge of the clock
  The /RAS and /CAS inputs no longer act as strobes
    But are instead, along with /WE, part of a 3-bit command

## Slide 11: Evolution of the DRAM Architecture
Synchronous DRAM
/CS | /RAS | /CAS | /WE | Address | Command
H | x | x | x | x | Command inhibit (No operation)
L | H | H | H | x | No operation
L | H | H | L | x | Burst Terminate: stop a read or write burst in progress
L | H | L | H | column | Read from currently active row
L | H | L | L | column | Write to currently active row
L | L | H | H | row | Activate a row for read and write
L | L | H | L | x | Precharge (deactivate) the current row
L | L | L | H | x | Auto refresh: Refresh one row of each bank, using an internal counter
L | L | L | L | mode | Load mode register: Address bus specifies DRAM operation mode.

## Slide 12: Evolution of the DRAM Architecture
Double Data Rate DRAM (DDR SDRAM)
  Doubles the data bandwidth available from single data rate SDRAM
    By transferring data at both edges of the clock

## Slide 13: DRAM Memory System Organization

## Slide 14: DRAM Memory System Organization
Channel

## Slide 15: DRAM Memory System Organization
Rank

## Slide 16: DRAM Memory System Organization
Bank

## Slide 17: DRAM Memory System Organization
Row

## Slide 18: DRAM Memory System Organization
column

## Slide 19: DRAM Memory System Organization
An Example

## Slide 20: Memory Modules
Single In-line Memory Module (SIMM)
  Contacts on either side of the bottom of the module are identical
  30-pin SIMMs
    Late 1980s and early 1990s
    8 or 9 signals for data bus+ cmds, addr, power, CS, …
  72-pin SIMMS
    32 to 64 bits data bus
Dual In-line Memory Module (DIMM)
  Contacts on either side of a DIMM are electrically different
  Late 1990s
  Physically larger than SIMMs
  64- or 72-bit-wide data bus interface
  Also referred to as Unbuffered DIMMs (UDIMMs)

## Slide 21: Memory Modules
Registered Dual In-line Memory Modules (RDIMMs)
  Alleviate the issue of electrical loading of large numbers of DRAM devices in a large memory system
  Use of registers that buffer the address and control signals at the interface of the memory module
  Registers greatly reduce the number of electrical loads that a memory controller must drive directly
  Buffering of the address and control signals introduces delays into the memory-access latency

## Slide 22: Memory Modules
Small Outline DIMM (SO-DIMM)
  Designed to fi t into the limited space found in mobile notebook computers

## Slide 23: Memory Modules
Different memory-module organizations
Serial presence detect (SPD)

## Slide 24: Memory System Topology
Determines the signal path lengths and electrical loading characteristics in the memory system

## Slide 25: Memory System Topology
Direct RDRAM System Topology