## Slide 1: Network Function Virtualization
Reference:

## Slide 2
NFV: Motivation and Problem Statement
  Trends in IT & Telecom Challenges
  NFV & SDN
Network Functions Virtualization
  Vision & Approach
  Benefits & Promises
  ETSI NFV ISG Working Groups & Reference Architecture
NFV Requirements and Challenges
  Performance, scalability, management, orchestration, resilience, security, portability, interoperability, etc.
  Ongoing Research efforts
Use Cases and Proof-of-Concepts
  CloudNFV, Service Chaining, VNF State Migration and Interoperability. Distributed-NFV, Multi Vendor vIMS, ForCES, Hardware Acceleration, Virtual EPC Gateway
Overview of Enabling Technologies
  Programmable vSwitches, Minimalistic OS (ClickOS), lightweight virtualization (Docker, LXC), Improving Linux I/O, x86 packet processing (Intel DPDK), vRouter (Vyatta), OpenStack, OPNFV
Outline

## Slide 3
NFV: Motivation and Problem Statement

## Slide 4
Complex carrier networks
With a large variety of proprietary nodes and hardware appliances.
Launching new services is difficult and takes too long
Space and power to accommodate
Requires just another variety of box, which needs to be integrated.
Operation is expensive
Rapidly reach end of life
Due to existing procure-design, integrate-deploy cycle.
Motivation and Problem Statement

## Slide 5
Motivation and Problem Statement

## Slide 6
NFV >>> Accelerating Transformation

## Slide 7
Scale and Virtualization in the Timeline

## Slide 8
High performance industry standard servers shipped in very high volume
Convergence of computing, storage and networks
New virtualization technologies that abstract underlying hardware yielding elasticity, scalability and automation
Software-defined networking
Cloud services
Mobility, explosion of devices and traffic
Trends

## Slide 9
Huge capital investment to deal with current trends
Network operators face an increasing disparity between costs and revenues
Complexity: large and increasing variety of proprietary hardware appliances in operator’s network
Reduced hardware lifecycles
Lack of flexibility and agility: cannot move network resources where & when needed
Launching new services is difficult and takes too long. Often requires yet another proprietary box which needs to be integrated
Challenges

## Slide 10
Commercial-off-the-shelf IT-platforms
allow to host a large variety of applications.
New virtualization technology allows to abstract HW,
enables elasticity, scalability and automation.
Network Technology suppliers already use such vTech,
but in a proprietary way.
Observation

## Slide 11
Network Functions Virtualization

## Slide 12
A means to make the network more flexible and simple by minimizing dependence on HW constraints
The NFV Concept

## Slide 13
Target

## Slide 14
Network Functions Virtualization is about implementing network functions in software - that today run on proprietary hardware - leveraging (high volume) standard servers and IT virtualization
Supports multi-versioning and multi-tenancy of network functions, which allows use of a single physical platform for different applications, users and tenants
Enables new ways to implement resilience, service assurance, test and diagnostics and security surveillance
Provides opportunities for pure software players
Facilitates innovation towards new network functions and services that are only practical in a pure software network environment
Applicable to any data plane packet processing and control plane functions, in fixed or mobile networks
NFV will only scale if management and configuration of functions can be automated
NFV aims to ultimately transform the way network operators architect and operate their networks, but change can be incremental
NFV :: Network Functions Virtualization

## Slide 15
Reduced equipment costs (CAPEX)
through consolidating equipment and economies of scale of IT industry.
Increased speed of time to market
by minimising the typical network operator cycle of innovation.
Availability of network appliance multi-version and multi-tenancy,
allows a single platform for different applications, users and tenants.
Enables a variety of eco-systems and encourages openness.
Encouraging innovation to bring new services and generate new revenue streams.
Flexibility to easily, rapidly, dynamically provision and instantiate new services in various locations
Improved operational efficiency
  by taking advantage of the higher uniformity of the physical network platform and its homogeneity to other support platforms.
Software-oriented innovation to rapidly prototype and test new services and generate new revenue streams
More service differentiation & customization
Reduced (OPEX) operational costs: reduced power, reduced space, improved network monitoring
IT-oriented skillset and talent
Benefits and Promises of NFV

## Slide 16
Switching elements: BNG, CG-NAT, routers.
Mobile network nodes: HLR/HSS, MME, SGSN, GGSN/PDN-GW.
Home networks: Functions contained in home routers and set top boxes to create virtualised home environments.
Tunnelling gateway elements: IPSec/SSL VPN gateways.
Traffic analysis: DPI, QoE measurement.
Service Assurance: SLA monitoring, Test and Diagnostics.
NGN signalling: SBCs, IMS.
Converged and network-wide functions: AAA servers, policy control and charging platforms.
Application-level optimisation: CDNs, Cache Servers, Load Balancers, Application Accelerators.
Security functions: Firewalls, virus scanners, intrusion detection systems, spam protection.
Some Use Case Examples Driving NFV

## Slide 17
Virtualization: Use network resource without worrying about where it is physically located, how much it is, how it is organized, etc.
Orchestration: Manage thousands of devices
Programmable: Should be able to change behavior on the fly.
Dynamic Scaling: Should be able to change size, quantity, as a F(load)
Automation: Let machines / software do humans’ work
Visibility: Monitor resources, connectivity
Performance: Optimize network device utilization
Multi-tenancy: Slice the network for different customers (as-a-Service)
Service Integration: Let network management play nice with OSS/BSS
Openness: Full choice of modular plug-ins
Note: These are exactly the same reasons why we need/want SDN.
So, why we need/want NFV(/SDN)?

## Slide 18
SDN+NFV, IT & Networking Growing Together

## Slide 19
SDN and NFV
SDN and NFV do NOT depend on each other

## Slide 20
NFV: re-definition of network equipment architecture
NFV was born to meet Service Provider (SP) needs:
Lower CAPEX by reducing/eliminating proprietary hardware
Consolidate multiple network functions onto industry standard platforms
SDN: re-definition of network architecture
SDN comes from the IT world:
Separate the data and control layers, while centralizing the control
Deliver the ability to program network behavior using well-defined interfaces
NFV vs SDN

## Slide 22
Global operators-led Industry Specification Group (ISG) under the auspices of ETSI
~150 member organisations
Open membership
ETSI members sign the “Member Agreement”
Non-ETSI members sign the “Participant Agreement”
Opening up to academia
Operates by consensus
Formal voting only when required
Deliverables: White papers addressing challenges and operator requirements, as input to SDOs
Not a standardization body by itself
Currently, four WGs and two EGs
Infrastructure
Software Architecture
Management & Orchestration
Reliability & Availability
Performance & Portability
Security
The ETSI NFV ISG
ETSI: European Telecommunications Standards Institute

## Slide 23
ETSI NFV High-level Architecture

## Slide 24
ETSI NFV Reference Architectural Framework

## Slide 25
Network Function (NF): Functional building block with a well defined interfaces and well defined functional behavior
Virtualized Network Function (VNF): Software implementation of NF that can be deployed in a virtualized infrastructure
VNF Set: Connectivity between VNFs is not specified, e.g., residential gateways
VNF Forwarding Graph: Service chain when network connectivity order is important, e.g., firewall, NAT, load balancer
NFV Infrastructure (NFVI): Hardware and software required to deploy, mange and execute VNFs including computation, networking, and storage.
NFV Orchestrator: Automates the deployment, operation, management, coordination of VNFs and NFVI.
NFV Concepts

## Slide 26
NFV
Requirements and Challenges

## Slide 27
General: Partial or full Virtualization, Predictable performance
Portability: Decoupled from underlying infrastructure
Performance: Conforming and proportional to NFs specifications and facilities to monitor
Elasticity: Scalable to meet SLAs. Movable to other servers.
Resiliency: Be able to recreate after failure. Specified packet loss rate, calls drops, time to recover, etc.
Security: Role-based authorization, authentication
Service Continuity: Seamless or non-seamless continuity after failures or migration
Service Assurance: Time stamp and forward copies of packets for Fault detection
Energy Efficiency Requirements: Should be possible to put a subset of VNF in a power conserving sleep state
Operational and Management Requirements: Incorporate mechanisms for automation of operational and management functions
Transition: Coexistence with Legacy and Interoperability among multi-vendor implementations
Service Models: Operators may use NFV infrastructure operated by other operators
NFV Framework Requirements

## Slide 28
Achieving high performance virtualized network appliances
portable between different HW vendors, and with different hypervisors.
Co-existence with bespoke HW based network platforms
enabling efficient migration paths to fully virtualized network platforms.
Management and orchestration of virtual network appliances
ensuring security from attack and misconfiguration.
NFV will only scale if all of the functions can be automated.
Appropriate level of resilience to HW and SW failures.
Integrating multiple virtual appliances from different vendors.
Network operators need to be able to “mix & match” HW,
hypervisors from different vendors,
and virtual appliances from different vendors
without incurring significant integration costs and avoiding lock-in.
Challenges

## Slide 29
End-to-end network services
Transparent management and orchestration
No place for one-size-fits-all solutions
Dynamic and heterogeneous new technologies
Handle different old and new characteristics
Impact on the other requirements:
Performance, resilience, security...
Maintain SLAs
Avoid disruptions!
Interoperability and Legacy Networks

## Slide 30
Different Levels
PFs, NFs, NFVI, NFV-FG
Monitoring, synchronization and trigger mechanisms in the event of failure of NFs
Correlated failures in NFV-FG
Chained resilience plans
Service Continuity
SLA minimum insurance
Zero impact vs. Measurable impact
Orchestration: NOT a single point of failure
Resilience

## Slide 31
New Threats
Virtualization Network Layer
Several identity layers and accounting
Protection of interfaces exposed by NFV architecture principles.
Secure separation and management of NF entities.
Heterogeneous network domains
NFVI shared resources
Isolation of VNF sets
User privilege resources access (APIs)
Mechanisms:
Control and verify the configuration of soft/hardware
Security

## Slide 32
In addition to high-performance / system-related challenges, networking challenges include:
NFV Resiliency
NFV-based service continuity.
Coexistence of virtualized and non-virtualized Network Functions (NFs)
Virtual Network Functions (VNF) Software (VM, Hypervisor) failure or congestion protection.
Monitoring, synchronization and trigger mechanisms in the event of failure of NFs.
NFV Control & Orchestration
Providing automation and elasticity.
NF Instance instantiation, scaling and migration.
End-to-end service setup, operation and monitoring.
Multi-technology support, and open interfaces.
NFV Security
Securing VNF instances.
Vulnerabilities introduced in the new virtualisation layer.
Protection of interfaces exposed by NFV architecture principles.
Secure separation and management of NF entities.
NFV Challenges for Networking Research

## Slide 33
Significant industry progress has been made to encourage growth of a commercial ecosystem for NFV, but research and education are also very important for overall and long term success.
NFV Research topics include:
Service chaining algorithms & NFV orchestration algorithms
Abstractions for carrier-grade networks and services
Performance studies (optimisation, scheduling, portability, reliability)
Security of NFV Infrastructure
Impacts of data plane workloads on computer systems architectures
Applying compositional patterns (i.e. Network Function Chains) for parallelism
Performance monitoring and reliability of network services
Energy-efficient NFV architectures
Service Assurance (e.g. test & diagnostics, predictive analytics, etc.)
New requirements on the NFV Infrastructure for supporting new types of VNFs
NFV Infrastructure federation
New network topologies and architectures
Tools and simulation platforms
NFV Research and Education

## Slide 34
NFV
Use Cases and Proof-of-Concepts

## Slide 35
Proof of Concepts - ETSI Evaluation Process

## Slide 36
Proof of Concepts – PoCs Completed
PoC#1 - CloudNFV Open NFV Framework Project
– Telefonica - Sprint - 6WIND - Dell - EnterpriseWeb – Mellanox - Metaswitch - Overture Networks - Qosmos - Huawei - Shenick
PoC#2 - Service Chaining for NW Function Selection in Carrier Networks
– NTT - Cisco - HP - Juniper Networks
PoC#3 - Virtual Function State Migration and Interoperability
– AT&T - BT - Broadcom Corporation - Tieto Corporation
PoC#4 - Multi-vendor Distributed NFV
– CenturyLink - Certes - Cyan - Fortinet - RAD
PoC#11 - Multi-Vendor on-boarding of vIMS on a cloud management framework
– Deutsche Telekom - Huawei Technologies - Alcatel-Lucent
PoC#5 - E2E vEPC Orchestration in a multi-vendor open NFVI environment
– Telefonica - Sprint - Intel - Cyan - Red Hat - Dell - Connectem
PoC#6 - Virtualised Mobile Network with Integrated DPI
– Telefonica - Intel - Tieto - Qosmos - Wind River Systems - Hewlett Packard
PoC#7 - C-RAN virtualisation with dedicated hardware accelerator
– China Mobile - Alcatel-Lucent - Wind River Systems - Intel
PoC#8 - Automated Network Orchestration
– Deutsche Telekom - Ericsson - x-ion GmbH - Deutsche Telekom Innovation Laboratories
PoC#9 - VNF Router Performance with DDoS Functionality
– AT&T - Telefonica - Brocade - Intel – Spirent
PoC#12 - Demonstration of multi-location, scalable, stateful Virtual Network Function
– NTT - Fujitsu - Alcatel-Lucent

## Slide 37
Proof of Concepts – PoCs Completed
PoC#14 - ForCES Applicability for NFV and integrated SDN
– Verizon - Telefonica - Mojatatu Networks – Cumulus Networks - University of Patras
PoC#15 - Subscriber Aware SGi/Gi-LAN Virtualization
– Telenor - ConteXtream - SkyFire Networks - Guavus - Redhat - HP
PoC#16 - NFVIaaS with Secure, SDN-controlled WAN Gateway
– AT&T - Telecom Italia - Netronome - Intel - ServiceMesh - PLUMgrid - Cisco Systems
PoC#19 - Service Acceleration of NW Functions in Carrier Networks
– AT&T - Ericsson - Avago Technologies - ARM - Tieto - Procera
PoC#22 - Demonstration of High Reliability and Availability aspects in a Multivendor NFV Environment
– AT&T - KDDI R&D Laboratories - Brocade – Hewlett Packard - Wind River System
PoC#23 - E2E orchestration of virtualized LTE core-network functions and SDN-based dynamic service chaining of VNFs using VNF FG
– SK Telecom - Hewlett Packard - Samsung - Telcoware
PoC#29 - Service orchestration for virtual CDN service over distributed cloud management platform
– KINX - IN-Soft - PIOLINK - ETRI
PoC#33 - Scalable Service Chaining Technology for Flexible Use of Network Functions
– NTT - ALAXALA Networks - Hitachi – Cisco Systems - NEC - Alcatel-Lucent

## Slide 38
Proof of Concepts – PoCs Completed

## Slide 39
Proof of Concepts – PoCs Completed

## Slide 40
NFV
Overview of Enabling Technologies

## Slide 41
Enabling Technologies
Minimalistic OS
ClickOS
Improving Linux I/O
Netmap, VALE, Linux NAPI
Programmable virtual switches / bridges
Open vSwitch
Exploiting x86 for packet processing
Intel DPDK
Some example start-ups
LineRate Systems, 6WIND, Midonet, Vyatta (bought by BCD)

## Slide 42
Conclusions

## Slide 43
Conclusions
NFV aims to reduce OpEx by automation and scalability provided by implementing network functions as virtual appliances
NFV allows all benefits of virtualization and cloud computing including orchestration, scaling, automation, hardware independence, pay-per-use, fault-tolerance, …
NFV and SDN are independent and complementary. You can do either or both.
NFV requires standardization of reference points and interfaces to be able to mix and match VNFs from different sources
NFV can be done now. Several of virtual functions have already been demonstrated by carriers.