## Slide 1: Reconfigurable Computing
Introduction

## Slide 2: Computing Paradigms
Processing architectures:
  General-purpose processors
    The Von Neumann Computer
  Domain-specific processors
    for a class of applications (e.g. multimedia, DSP)
  Application-specific processors
    for one application
  Reconfigurable processors

## Slide 3: The Von Neumann Computer
Principle
  In 1945, the mathematician Von Neumann (VN):
  A computer could have a simple structure,
  capable of executing any kind of program,
  given a properly programmed control unit,
  without the need of hardware modification.

## Slide 4: The Von Neumann Computer
Structure
  A memory for storing program and data and instructions.
  A control unit (control path) featuring a program counter for controlling program execution
  An ALU for program execution
Datapath
Control path
Processor or
Central processing unit
Data
and
Instructions
Address
register
Memory
Instruction
register
PC
Data
Address
Registers

## Slide 5: The Von Neumann Computer
Coding
  A program is coded as a set of instructions to be
  sequentially executed
Program execution
  Instruction Fetch (IF): The next instruction to be executed is fetched from the memory
  Decode (D): The instruction is decoded to determine the operation
  Read operand (R): The operands are read from the memory
  Execute (EX): The required operation is executed on the ALU
  Write result (W): The result of the operation is written back to the memory
  Instruction execution in Cycle (IF, D, R, EX, W)

## Slide 6: The Von Neumann Computer
Advantage:
  Flexibility: any well coded program can be executed
Drawbacks:
  Speed efficiency: Not efficient, due to the sequential program execution
    They cannot even drive their display (need graphics accelerator)
  Resource efficiency: Only one part of the hardware resources is required for the execution of an instruction. The rest remains idle
  Memory access: Memories are about 10 time slower than the processor
  Energy efficiency: MOPS/W
  Speed drawbacks are compensated using high clock speed, pipelining, caches, instruction pre-fetching, etc.

## Slide 7: The Von Neumann Computer
Sequential execution
  tcycle = cycle execution time
One instruction needs tinstruction = 5*tcycle
3 instructions: in 15*tcycle
Pipelining:
One instruction needs tinstruction = 5*tcycle
  no improvement
3 instructions: in 7*tcycle in the
ideal case.
 Increased throughput
Even with pipeline, cache, etc., execution remains sequential.

## Slide 8: Multi-Core/Many-Core
Goal:
  Using parallelism in the VN computer.
Characteristics:
  Applicable to applications with parallel algorithms
  Memory access still limited (techniques: local memory, shared memory, …)
  Limited speedup

## Slide 9: Multi-Core/Many-Core Speedup
Amdahl’s Law:
Serial% = 6.7%
N = 16 Cores, Speedup = 8
Serial% = 20%
N = 6 Cores,
Speedup = 3
Speedup =

## Slide 10: Multi-Core Speedup
Amdahl’s Law:
  Speedup by multi-cores is limited.
  Even when the number of cores is large, it is limited by the serial part:
    If 88% of the operations are not parallelizable, (regardless of the number of cores):
    Max speedup = 1/(0.88) = 1.136 !
    To achieve 50x speedup, at least 98% of the application must be appropriate for substantial acceleration.

## Slide 11: Domain-Specific Processors
Goal:
  Overcome part of the drawbacks of the VN computer.
Characteristics:
  Optimized datapath for a given class of applications
    Example: DSP
    Applications usually multiply accumulate (MAC)-dominated:
      A  A + (B * C)
    Datapath optimized to execute one or many MACs in only one cycle.
  Instruction fetching/decoding overhead removed for some operations
  Fewer memory access
  Special support for efficient looping
    Special loop or repeat instruction

## Slide 12: MAC on a VN Machine
  Fetch MUL
  Decode MUL
  Read operand
  Multiply
  Store result (B*C)
  Fetch ADD
  Decode ADD
  Read the stored result (B*C)
  Add with the accumulated value (A + B*C)
  Store

## Slide 13: Loops on a VN Machine
Instruction cycles (fetch, decode, …) for:
  Updating loop counter
  Testing loop counter
  Jumping back to the top of the loop

## Slide 14: Domain-specific processors
The hardware contains:
  One or more MAC-Units
  Multi-ported on-chip and off-chip memories
  Multiple on-chip busses
  Address generation unit supporting addressing modes tailored for DSP-applications

## Slide 15: ASIP
Application-Specific Instruction Set Processors:
  Instruction set is customized to a specific domain/application
    DSP, neural networks, …
  Can be classified as domain-specific
  Xtensa from Tensilica (Acquired by Cadence in 2013)
    A processor core which lets the system designer:
      select and size features for a given application
      define new instructions.

## Slide 16: Application-Specific Processors
Optimize the complete circuit for a specific function
  DSPs have VN architecture.
  with a degree of application-specific features
Example: ASIC: Application-Specific Integrated Circuit.
  Optimization is done by implementing the inherent parallel structure on a chip
  The data path is optimized for only one application.
  Instruction fetching and decoding overhead is removed
  Memory access is limited:
    Directly processing the input data flow

## Slide 17: Application-Specific Processors
ASIC Example:
Implementation of a VN computer:
  if (a < b) then
  {
    d = a+b;
    c = a*b;
  }
  else
  {
    d = a+1;
    c = b-1;
  }
At least 3 instructions
run-time >= 3*tinstruction
ASIC implementation:
Complete execution in
parallel in one clock cycle
run-time = tclock= delay of longest path from input to output

## Slide 18: ASIC as Accelerator
ASIC as a coprocessor

## Slide 19: ASIC as Accelerator
High manufacturing cost

## Slide 20: ASIC as Accelerator
High manufacturing cost

## Slide 21: Development Complexity
[Peckham13]

## Slide 22: Conclusion
Von Neumann computer:
  General purpose, used for any kind of function
DSPs
  Designed for a class of applications
ASICs
  Tailored for one application

## Slide 23: Conclusion
Von Neumann computer:
  General purpose, used for any kind of function
    High degree of flexibility
  Speed and energy efficiency problem
  Some restrictions on the program coding and execution scheme
    Programs have to adapt to the machine
DSPs
  Designed for a class of applications
  Flexibility and efficiency only for a given class of applications
ASICs
  Tailored for one application
  Very efficient in speed and resource
    Hardware adapts to the application
  Cannot re-adapt to a new application
    Not flexible

## Slide 24: Reconfigurable Computing
The ideal device should combine:
  Flexibility of the VN computers
  Efficiency of ASICs
The ideal device should be able to
  Optimally implement an application in acceptable time
  Re-adapt to allow the optimal implementation of a new application
We call such a device a reconfigurable device.

## Slide 25: Reconfigurable Computing
The ideal device should combine:
  Flexibility of the VN computers
  Efficiency of ASICs
The ideal device should be able to
  Optimally implement an application in acceptable time
  Re-adapt to allow the optimal implementation of a new application
We call such a device a reconfigurable device.
Definition: Reconfigurable computing: study of computations involving reconfigurable devices.
Architectures
Algorithms
Applications

## Slide 26: RCS Definitions
  “Reconfigurable computing refers to any information processing system in which blocks of hardware can be reorganized or repurposed to adapt to changing dataflows or algorithms.”
    Ron Wilson, EE Times
  “A reconfigurable computer is a device which computes by using post-fabrication spatial connections of computable elements.”
    Andre DeHon
  “Reconfigurable devices contain an array of computational elements whose functionality is determined through multiple programmable configurations.”
    Compton and Hauck
  “On-the-fly ASIC”
    Kurdahi
  “Soft hardware”
    Lyke
All are correct:
  Better to understand by example

## Slide 27: Main Idea
[Lyke15]
Benefits:
  Lower cost
  Extensibility

## Slide 28: Reconfigurable Computing
Configuration:
  A device is configured when its functionality is set.
    ASIC is configured when the circuit is fabricated.
    Gate arrays/structured ASIC are configured when the routing is defined.
      Structured ASIC: ASICs that may be repurposed with a single mask layer (or a few) instead of several dozen
      Intel eASIC N5X
    Microprocessor is configured when an instruction is read from memory.
       Microprocessors bind functionality at every cycle.

## Slide 29: Uncommitted Gate Array

## Slide 30: Committed Gate Array

## Slide 31: Reconfigurable Computing
Configuration:
  The amount of programmability:
    ASIC: can perform exactly one task (not programmable)
    GPP: can perform a wide variety of operations:
      ISA defines the number of operations that can be performed at a given time.
      64 bits
    FPGA: functionality is dedicated by bitstream:
      10 - >1000 million bits
        Virtex-II Pro XC2VP125: 43 million bits, Virtex-7: 112 million bits, Virtex UltraScale+: 1024 million bits)

## Slide 32: Reconfigurable Computing
Reconfigurabilty:
  The ability to continually change the functionality of the device.
    But microprocessors are not usually considered as reconfigurable devices.
Reconfiguration:
  The process of changing the structure of a reconfigurable device (at run-time or off-line)

## Slide 33: Flexibility vs Efficiency
Perfromance
F
l
e
x
i
b
i
l
i
t
y
Von Neumann
General purpose
computing
DSP
Domain-specific
computing
ASIC
Application
-specific
computing
Reconfigurable
systems
Reconfigurable
computing

## Slide 34: A Decade of Progress
  200x More Logic
    Plus memory, μP etc.
  40x Faster
  50x Lower Power
  500x Lower Cost
[Areiba08]
CLB Capacity
Speed
Power per MHz
Price
Virtex &
Virtex-E
XC4000
100x
10x
1x
Spartan-2
1000x
Virtex-II &
Virtex-II Pro
Virtex-4
XC4000 &
Spartan
Spartan-3
'91 '92 '93 '94 '95 '96 '97 '98 '99 '00 '01 '02 '03 '04
Year
Courtesy: Richard Sevcik, Xilinx

## Slide 35: Three Decades of Progress
[Trimberger18]
Capacity:
  logic cell count
  10,000x
Speed:
  same-function performance in programmable fabric.
  100x
Price:
  per logic cell
  1000x
Power:
  per logic cell
  1000x

## Slide 36: High performance parallel computing
Traditional parallel implementation flow
Application
1
2
3
4
5
6
7
Virtual Topology
Physical Topology
1
2
3
4
Exploiting reconfigurable topology
Application
1
2
3
5
6
7
4
Virtual Topology
1
2
3
5
6
4
7
Physical Topology

## Slide 37: The main question
A reconfigurable device is a piece of hardware and
A hardware can never change after fabrication
Then
How is a reconfigurable device made?

## Slide 38: Microprocessor-Based Systems (Temporal)
  Generalized to perform many functions well
  Operates on fixed data sizes.
  Inherently sequential
    Constrained even with multiple data paths.
Data Storage
(Register File)
ALU
A
B
C
64

## Slide 39: A Simple Reconfigurable Circuit
  Functional unit optimized to perform a special task.
Functional
Unit
A
B
H
L
if (A > B) {
H = A;
L = B;
}
else {
H = B;
L = A;
}

## Slide 40: Example: Bubblesort (Spacial)
  Adapt interconnect to problem.
  Take advantage of parallelism.
A
B
H
L
A
B
H
L
A
B
H
L
A
B
H
L
A
B
H
L
Highest Value
Lowest Value

## Slide 41: ASIC as Accelerator
Increasing design cost + manufacturing cost
Decreasing life cycle
   Decreasing number of wafer starts

## Slide 42: ASIC Starts vs. FPGA Starts

## Slide 43: More Life Cycle in FPGAs

## Slide 44: FPGA Replacing ASIC
rDPA:
  Reconfigurable Data Path Array

## Slide 45: Conclusion
ASSP:
  Application-Specific Standard Parts:
  As ASIC but more general-purpose device (for many system design houses.
  Examples:
  Interface chips (USB, …)
[www.altera.com]

## Slide 46: Cost-Volume Curve
  Increasing manufacturing costs increases NRE costs
   Crossover point shifts to right with every new technology node.
Volume
Cost
PLD
ASIC
Cross-over volume

## Slide 47: Cost-Volume Curve
   For many users, ASIC is not a choice anymore.
   ASIC for very high volume or very high performance (millions of units [Trimberger18])
    Few chips: cryptocurrency miners, image processing chips for TVs
Volume
Cost
PLD
ASIC
Cross-over volume

## Slide 48: Speedups
Reported speedups:
  Up to x28500
[Cardoso11]

## Slide 49: Speedups
SR: Super-Resolution:
  Construction of high-resolution images from several low-resolution observations
  Speedup: up to 4 orders of magnitude
[Georgis16]

## Slide 50: Efficiency
[ExtremeTech16]

## Slide 51: Efficiency

## Slide 52: Spiking Neural Neworks
[Isik23]

## Slide 53: References
  [Areiba08] Areiba, “Reconfigurable Computing Systems,” Lecture Slides.
  [Bobda07] Bobda, Reconfigurable Computing Systems,” Lecture Slides.
  [Cardoso11] Cardoso and Hubner, Reconfigurable Computing: From FPGAs to Hardware/Software Codesign, Springer, 2011.
  [Peckham13] Clarence Peckham, “GPGPUs Stake Out Territory beside FPGAs for Military Signal Processing,” COTS Journal, April 2013.
  [Georgis16] Georgis, Georgios, George Lentaris, and Dionysios Reisis. "Acceleration techniques and evaluation on multi-core CPU, GPU and FPGA for image processing and super-resolution." Journal of Real-Time Image Processing (2016): 1-28.
  [ExtermeTech16] Joel Hruska, “Intel launches Stratix 10: Altera FPGA combined with ARM CPU, 14nm manufacturing,” ExtremeTech, 2016.

## Slide 54: References
  [Kaeli15] Kaeli, et al, Heterogeneous Computing with OpenCL 2.0, Morgan Kaufmann, 2015.
  [Lyke15] Lyk, et al, “An Introduction to Reconfigurable Systems,”, Proceedings of the IEEE, Vol. 103, No. 3, March 2015.
  [Trimberger18] Trimberger, Three Ages of FPGAs: A Retrospective on the First Thirty Years of FPGA Technology, IEEE Solid-State Circuits Magazine 10.2 (2018): 16-29.
  [Isik23] Isik, “A Survey of Spiking Neural Network Accelerator on FPGA,” arXiv preprint arXiv:2307.03910, (2023).