## Slide 1: Heterogeneous FPLDs

## Slide 2: Heterogeneous Logic Blocks
Mixture of two different sizes of LUTs:
  Larger LUT and cluster sizes: higher speed
  Smaller sizes: more area efficient
    Up to the CAD tool to select the resource
Mixture of PAL-like LBs and LUT-based LBs:
  PAL blocks: improved circuit speed
  LUT blocks: area and power efficiency
Mixture of “specific-purpose logic” and general-purpose LBs:
  SP LBs: superior area, speed, and power consumption
  If the function is not used, the silicon area is wasted

## Slide 3: Heterogeneous Logic Blocks
Key questions:
  Which kinds of SP functions?
  What should be the ratio: SP/GP?
  What can be done about SP LBs not used in a specific application?
    Rose’s golden rule: “build structures that are always useful, even if that use is less than perfectly efficient.”
    “The more useful a hard structure is, across a wider range of applications, then the greater its net benefit - provided the cost of the extra functionality is not excessive.”
      Rose. Hard vs. Soft: The Central Question of Pre-Fabricated Silicon. In Proceedings of the 34th International Symposium on Multiple-Valued Logic (ISMVL’04), 2004.

## Slide 4: Hard Blocks
Common hard blocks in modern FPGAs:
  Memory
  Multipliers
  MAC for DSP applications
  Microprocessors
  …

## Slide 5: Hard Blocks
Logic Blocks vs. SP Blocks

## Slide 6: Hard Blocks
Logic Blocks vs. SP Blocks

## Slide 7: Hard Blocks
Logic Blocks vs. SP Blocks

## Slide 8: Hard Blocks
Logic Blocks vs. SP Blocks

## Slide 9: Embedded Memories

## Slide 10: Virtex 7
  Block RAMs are fundamentally 36 Kb in size; each block can also be used as two independent 18 Kb blocks.

## Slide 11: Xilinx FPGAs
 | Spartan-6 | Artix-7 | Kintex-7 | Virtex-7 | Kintex UltraScale | Virtex UltraScale
Logic Cells | 147,443 | 215,360 | 477, 760 | 1,954,560 | 1,160,880 | 4,407,480
BlockRAM | 4.8Mb | 13Mb | 34Mb | 68Mb | 76Mb | 115Mb
DSP Slices | 180 | 740 | 1,920 | 3,600 | 5,520 | 2,880
Transceiver Count | 8 | 16 | 32 | 96 | 64 | 104
Transceiver Speed | 3.2 Gb/s | 6.6 Gb/s | 12.5 Gb/s | 28.05 Gb/s | 16.3 Gb/s | 32.75 Gb/s
Total Transceiver Bandwidth (full duplex) | 50 Gb/s | 211 Gb/s | 800 Gb/us | 2,784 Gb/s | 2,086 Gb/s | 5,101 Gb/s
I/O Pins | 576 | 500 | 500 | 1,200 | 832 | 1,456

## Slide 12: Heterogeneous Logic Blocks
Each M10K (M20K) block in Intel Cyclone:
  10Kb bits if used as memory
    Dual port RAM, ROM, FIFO, …
  Can be used as logic

## Slide 13: Cyclone M10K Blocks
M10K (Bits)
256 × 40 or 32
512 × 20 or 16
1K × 10 or 8
2K × 5 or 4
4K × 2
8K × 1
In single- or dual-port mode

## Slide 14: Configuration as Memory
A[12..0]
D0
8kx1
D[31..0]
A[7..0]
256x32
A[8..0]
D[15..0]
512x16
A[9..0]
D[7..0]
1028x8

## Slide 15: Configuration as Memory
Can be used independently
Can be combined for a larger memory
A[9..0]
D[7..0]
1024x8
A[9..0]
D[7..0]
1024x 8
D[15..0]
A[9..0]

## Slide 16: Intel Cyclone
Notes: Cyclone III devices feature OCT to provide I/O impedance matching and termination capabilities.
OCT helps to prevent reflections and maintain signal integrity while minimizing the need for
external resistors in high pin-count ball grid array (BGA) packages.

## Slide 17: Cyclone V

## Slide 18: Memory Modes
Simple dual-port mode:
  Supports simultaneous read and write operation to different locations.
True dual-port mode:
  Supports any combination of two-port operations:
    two reads,
    two writes,
    one read and one write,
  at two different clock frequencies.

## Slide 19: Altera Stratix II Embedded Memory

## Slide 20: TriMatrix Memory Structure

## Slide 21: حافظه در Cyclone
دو نوع:
  بلوک‌های M10K:
    8 کیلوبیت:
      هر 4 بیت: 1 بیت توازن (parity)
    10 کیلوبیت داده
    Single/dual port
    (در Cyclone IV:
      بلوک‌های M9K
      بلوک‌های M144K)
  MLAB:
    640-bit dual port RAM
      هر ALM: 32 x 2
      برای shift register و FIFO کوچک
پیکربندی ( تعداد بیت × تعداد کلمات )
40 × 256
32 × 256
20 × 512
16 × 512
10 × k 1
8 × k 1
5 × k 2
4 × k 2
2 × k 4
1 × k 8

## Slide 22: بلوک‌های منطقی و معماری اتصالات

## Slide 23: حافظه بلوکی در تراشه های UltraScale+ شرکت Xilinx
  بلوک‌های UltraRAM:
    288 کیلوبیت:
    4096 × 72 بیت
تراشه ها:
  Kintex UltraScale+ (تا 22/5 مگابیت)
  Zynq UltraScale+ (تا 22/5 مگابیت)
  Virtex UltraScale+ (تا 360 مگابیت)

## Slide 24
تکلیف

## Slide 25: Configuration as Logic Function
Remember:
  What can be done about SP LBs not used in a specific application?
Can be used as a big LUT
  E.g. Square root: 8-input, 8-output memory module
Advantages (vs. small LUT implementation):
  Higher speed
  Predictable speed
Can implement either independently or combined to implement larger functions

## Slide 26: Applications of Embedded Memory
داده | آدرس
0 | 0
1 | 1
1/4 | 2
1/7 | 3
2 | 4
2/2 | 5
... | ...
n | N

## Slide 27: Applications of Embedded Memory
تابع سیگموید

## Slide 28: Applications of Embedded Memory
  4x4 Multiplier
    or any complex math function

## Slide 29: Applications of Embedded Memory
  4x4 Multiplier
    or any complex math function
For larger multipliers, can use several 4x4 mults + adders

## Slide 30: Applications of Embedded Memory
دقت محاسبه:
  جذر اعدادی که در جدول نیستند (1/5):
    گرد کردن
    کوتاه کردن
    تقریب خطی
      دقیق‌تر
      سخت‌افزار اضافی
داده | آدرس
0 | 0
1 | 1
1/4 | 2
1/7 | 3
2 | 4
2/2 | 5
... | ...
n | N

## Slide 31: Applications of Embedded Memory
Constant multiplication
  For DSP and control systems
  Constant value determines memory content patterns
  If constant is changed, can load new values
  Multiplication precision can be set (cost saving)

## Slide 32: FIR (Finite Impulse Response) Filter

## Slide 33: Applications of Embedded Memory
Transcendental functions
  sin, cos, …, logarithm, …
    Costly/complex hardware implementation
  Arguments: α  address lines
  Results: sin(α)  data lines

## Slide 34: پیاده­سازی ماشین حالت با حافظه
ماشین فروش شکلات:
حالت جاری |  |  | ورودی ها |  | حالت بعدی |  | خروجی
 | S1 | S0 | D | P | S1 | S0 | DOOR
(start) | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 0 | 1 | 0
 |  |  | 1 | 1 | X | X | X
(P200) | 0 | 1 | 0 | 0 | 0 | 1 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 1 | 0 | 0
 |  |  | 1 | 1 | X | X | X
(P400) | 1 | 0 | 0 | 0 | 1 | 0 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 1 | 1 | 0
 |  |  | 1 | 1 | X | X | X
(full) | 1 | 1 | 0 | 0 | 1 | 1 | 1
 |  |  | 0 | 1 | 1 | 1 | 1
 |  |  | 1 | 1 | 1 | 1 | 1
 |  |  | 1 | 0 | 1 | 1 | 1

## Slide 35: پیاده­سازی ماشین حالت با حافظه
ماشین فروش شکلات:
حالت جاری |  |  | ورودی ها |  | حالت بعدی |  | خروجی
 | S1 | S0 | D | P | S1 | S0 | DOOR
(start) | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 0 | 1 | 0
 |  |  | 1 | 1 | X | X | X
(P200) | 0 | 1 | 0 | 0 | 0 | 1 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 1 | 0 | 0
 |  |  | 1 | 1 | X | X | X
(P400) | 1 | 0 | 0 | 0 | 1 | 0 | 0
 |  |  | 0 | 1 | 1 | 1 | 0
 |  |  | 1 | 0 | 1 | 1 | 0
 |  |  | 1 | 1 | X | X | X
(full) | 1 | 1 | 0 | 0 | 1 | 1 | 1
 |  |  | 0 | 1 | 1 | 1 | 1
 |  |  | 1 | 1 | 1 | 1 | 1
 |  |  | 1 | 0 | 1 | 1 | 1
آدرس | محتوای حافظه |  | 
0000 | 0 | 0 | 0
0001 | 1 | 1 | 0
0010 | 0 | 1 | 0
0011 | 0 | 0 | 0
0100 | 0 | 1 | 0
0101 | 1 | 1 | 0
0110 | 1 | 0 | 0
0111 | 0 | 0 | 0
1000 | 1 | 0 | 0
1001 | 1 | 1 | 0
1010 | 1 | 1 | 0
1011 | 0 | 0 | 0
1100 | 1 | 1 | 1
1101 | 1 | 1 | 1
1110 | 1 | 1 | 1
1111 | 1 | 1 | 1

## Slide 36: پیاده­سازی ماشین حالت با حافظه
  حافظه باید همگام با کلاک باشد

## Slide 37: Applications of Embedded Memory
Code converters

## Slide 38: Computation-Oriented Tiles

## Slide 39: 18x18 Multipliers
For computational applications and DSP

## Slide 40: Multipliers in Altera Cyclone V
Multipliers in DSP blocks

## Slide 41: Embedded Multipliers in Cyclone V
Cyclone 10:
  Up to 200 DSP blocks but with 54 x 54 bit floating point multipliers

## Slide 42: Embedded Multipliers
Variable Precision DSP Blocks:
  Can configure each embedded multiplier as
    one 27 × 27 or
    two 18 × 18 or
    three 9 × 9.
  For > 27 × 27, the Quartus Prime software cascades.
  No restriction on the data width
    but the greater the data width, the slower the multiplication process.
  Can also implement soft multipliers using memory blocks.
     Increase the number of multipliers.
Other features of DSP blocks:
  18 × 18 bit internal coefficient register banks
  Adder
  64-bit accumulator

## Slide 43: Multiplier Block Architecture

## Slide 44: 9-Bit Mode

## Slide 45: DSP Blocks

## Slide 46: Stratix DSP Blocks

## Slide 47: Stratix II DSP Blocks

## Slide 49: Ratio-Based Architectures
If multipliers not needed by an application, the multipliers provide little benefit.
  Solution: multiple sub-families within a device family with different ratios of soft logic to hard-logic.
  Designer can select the device with the most appropriate ratio
     Minimize “wasted” area
     FPGA vendor must support a larger number of devices
462
soft/hard ratio
190
272

## Slide 50: Embedded Processors

## Slide 51: Embedded System Design
  In the past, CPU and its peripheral: as discrete chips
     High area cost,
     Low reliability.
  For relatively small amount of memory, integrated memory in FPGA is used.

## Slide 52: SoPC
SoC:
  A chip that integrates the major functional elements of a complete end product.
Complex FPGAs:
  CPU
  Memory
  Arithmetic units (multipliers, …)
  Peripheral modules
  Logic
   Whole system on a programmable chip (SoPC)

## Slide 53: Challenges
Challenges:
  Decision on hardware/software partitioning
  Design environment must support hardware/software co-verification.

## Slide 54: Microprocessor Cores
Two types:
  Hard Core
    Implemented as hardwired component
      PowerPC, then ARM in Xilinx
      ARM in Intel
      MIPS in QuickLogic
  Soft Core
    Configure logic blocks to act as microprocessor(s)
      MicroBlaze in Xilinx
      NiosII/Nios V in Intel
      Q90C1 in QuickLogic

## Slide 55: Soft Processor Core
Soft Processor Core:
Disadvantages:
  Generally slower
  Larger
Advantage:
  Can often be customized to exactly suit the needs of the application
     Gains back some of the lost performance and area efficiency.

## Slide 56: Soft Microprocessor Cores
Firm or Soft:
  Soft: if in the form of RTL that will be synthesized
  Firm: if placed and routed
Peripherals in soft or firm form:
  E.g. Memory controllers, interrupt controllers, communication functions, timer counters.
  Refer to library of FPGA vendor
Xilinx
  MicroBlaze: 32-bit microprocessor (~1000 logic cells)
  PicoBlaze: 8-bit microprocessor (~150 logic cells)
Intel:
  NIOS V:
    32-bits
    Based on RICS V

## Slide 57: Dedicated Logic on FPGAs

## Slide 58: Dedicated Logic on FPGAs
Interconnect protocols

## Slide 59: Dedicated Logic on FPGAs
Kintex 7 vs. Spartan 3 both from Xilinx

## Slide 60: Recent Dedicated Blocks
AI Engine in “Versal ACAP” device
  ACAP: Adaptive Compute Acceleration Platform
  Array of VLIW processors with SIMD vector units
    Highly optimized for compute-intensive applications:
      5G wireless and AI applications

## Slide 61: Recent Dedicated Blocks
Heterogeneous Integration of Three Types of Programmable Engines

## Slide 62: Recent Dedicated Blocks
Heterogeneous Integration of Three Types of Programmable Engines

## Slide 63: Recent Dedicated Blocks
Intelligent Engines

## Slide 64: Recent Dedicated Blocks
AI Engine

## Slide 65: References
[Xilinx/AMD] www.xilinx.com, www.amd.com
[Altera/Intel] www.altera.com, www.intel.com
م. صاحب‌الزمانی، طراحی کامپیوتری سیستم‌های دیجیتال، نشر شیخ بهایی، 1398