## Slide 1: Math Doesn’t Have to be Hard: Logic Block Architectures to Enhance Low-Precision Multiply-Accumulate on FPGAs
Andrew Boutros1,2, Mohamed Eldafrawy1, Sadegh Yazdanshenas1 & Vaughn Betz1,2
1Department of Electrical and Computer Engineering, University of Toronto, Toronto, ON, Canada
2Vector Institute, Toronto, ON, Canada
February 25, 2019
Notes: Since FPGAs were introduced in 1980s, researchers and FPGA vendors have been trying to answer one question which was the driving force for all FPGA architectural enhancements over the past 35 years.

## Slide 2: Can FPGAs do better?
in deep learning?
Base station: https://www.businesswire.com
Network switch: https://www.techpartz.com
Autonomous car: https://news.psu.edu
Notes: This question is CAN FPGAS DO BETTER?
- For every new chip, FPGA architects are coming up with ideas to improve the performance, power efficiency and area efficiency of FPGAs.
- This has led to introducing memory blocks, DSP blocks, sophisticated routing architectures and most recently Networks on chip!
- FPGAs are getting more complex and heterogeneous trying to adapt to wide range of applications while preserving their general purpose nature.
- In this study we have asked ourselves the same questions. CAN FPGAS DO BETTER? But this time in deep learning.

## Slide 3: Deep Learning: Accuracy vs. Compute
Chart: Top-1 Error (%)
| AlexNet (2012) | GoogleNet (2014) | ResNet-152 (2015) | AmoebaNet-A (2018)
Error (%) | 16.4 | 6.67 | 4.49 | 3.4
Operations | 1.14 | 1.5 | 11.3 | 104
Neural networks for image processing 
Highly accurate models:
  Computational cost
  power
Notes: Deep learning, have gained a lot of attention in the recent years.
Being able to solve complex problems such as image classification and speech recognition have encourage a huge amount of research both on the algorithm development side and the hardware acceleration side.
A key metric in deep learning is the network’s accuracy. Researchers are always publishing state-of-the-art deep learning models that are able to achieve higher accuracies than their predecessors.
However, accuracy doesn’t come for free. Highly accurate models tend to have high computational cost. Requiring hardware platforms that can provide high performance and power efficiency.
And power efficiency is very important, specially, when it comes to devices with tight power budgets like smartphones.

## Slide 4: Efficient Inference: Low-Precision DNNs
One way of reducing computations: Low-precision
Lowering the precision of weights/activations:
  Reduce memory bandwidth
  Reduce computational energy
  Reduce multiply-accumulate area
How is accuracy affected by lowering precision?
Notes: One way of decreasing the computational complexity of deep neural networks is to reducing the precision of their weights and activations.
So, what are the actual gains of doing so.
First this reduces the memory bandwidth requirements of the hardware, reduce the multiply-accumulate area and the computational energy
However, the main reason for increasing computational complexity is to increase network’s accuracy. So, an important question is: how is accuracy affected by lowering precision?!!!

## Slide 5: Deep Learning: Best Precision?
Lowering precision can degrade accuracy
But network re-engineering can recover accuracy
Most hardware-efficient precision?
  No single answer
  Depends on accuracy target, application, model …
  Precision from 4 – 9 bits is pareto-optimal for many target accuracies1,2
J. Fowers et al., “A Configurable Cloud-Scale DNN Processor for Real-Time AI” in ISCA 2018
M. Bott et al., “FINN-R: An End-to-End Deep-Learning Framework for Fast Exploration of Quantized Neural Networks ” in TRETS 2018
Notes: Decreasing precision can actually degrade accuracy which is in some applications not tolerable.
Recent work, shows that going from single-precision floating point to 16-bit fixed point can degrade the top-1 accuracy of the network on the image net dataset by 0.5%
However, some techniques could be used to recover this accuracy loss. For instance, increasing layer sizes or using block floating point with small mantissa instead of fixed point
So, what is the most hardware-efficient precision?
Well, there is no single answer, it depends on the accuracy target, application, and model being used.
However, recent work has shown that precisions form 4 – 9 bits is pareto-optimal for many target accuracies

## Slide 6: Low-Precision on FPGAs
FPGAs naturally adapt to precision variation
  Reconfigurable
  Variable bit-width data paths
  Advantageous to GPU
DSPs are good for large multiplies (Ex: 18-bit)
  Fast, compact and reasonably numerous
    18x18 multiplier = 150 ALMs
  But very limited (5% of core area in DSP-rich devices)
Are DSPs as good for low-precision multiplies?
  24x more 4-bit multiplies using logic blocks
Can logic blocks do even better at low-precision?
24x more 4-bit
multiplies
DSP blocks
logic blocks
Notes: The good news is that FPGAs naturally adapt to precision variation. Since, they are reconfigurable and have variable bit-width data paths.
Multiplies and multiply accumulates are mostly carried out using DSP blocks. And currently DSP blocks have limited precisions available
The smallest precision available in Stratix-10 DSP block is 18x18. At this bit width, multipliers are more efficiently implemented using DSPs. An 18x18 multiplier will need 150 ALMs to be implemented using soft logic. In addition, they will never be as fast as the DSPs at this bit width.
But are DSPs as good for low-precision multiplies?
Well at this precision, you can implement 24x more 4-bit multiplies using logic blocks than DSPs. While also at this size there is no difference in speed.
Results on Arria 10 fastest speed grade:
18x18 multiplication: 11520x (DSP multipliers @ 548 MHz) vs. 17834x (logic block multipliers @ 257 MHz) LB:DSP  1.55x
4x4 multiplication: 11520x (DSP multipliers @ 548 MHz) vs. 280000x (logic block multipliers @ 617 MHz) LB: DSP  24.3x

## Slide 7: Multiplication: DSP Blocks vs. Logic Blocks
On Arria 10 fastest speed grade:
  18x18 multiplication:
    11520x (DSP multipliers @ 548 MHz)
    17834x (logic block multipliers @ 257 MH4)
     LB:DSP  1.55x
  4x4 multiplication:
    11520x (DSP multipliers @ 548 MHz)
    280000x (logic block multipliers @ 617 MHz)
    LB: DSP  24.3x

## Slide 8: Logic Block Multipliers
Notes: Logic blocks are highly flexible and are the most ubiquitous recourse on an FPGA. But how efficient are they when it comes to multipliers implementation?
First we need to know how are the multiplier currently mapped to the state of the art logic block architectures.
Then we can look for potential rooms for improvement.

## Slide 9: Baseline: Stratix 10-like Logic Block
Architecture specs:
8 distinct inputs
Fracturable LUT: Used as
  One 6-LUTS
  two 4-LUTs
  One 4-LUT and two 3-LUTs
2 bits of arithmetic
4 optionally registered outputs
Notes: The baseline state-of-the-art logic block architecture we are using for this study in the startix-10 architecture. Here we are showing a stratix-10like logic block. This logic block has 8 distinct inputs, a 6-input fracturable LUT that can be used a one 6-input LUT or two 5-input LUTs or smaller having a maximum of 8 distinct inputs. In addition, the LUT Is used as 4-input LUTs when in arithmetic mode providing two bits of addition per ALM. Finally, the ALM has for outputs which can be optionally registered.

## Slide 10: Multiplication Operation
Multiplication Steps:
Partial products generation (LUTs)
Partial products reduction (Adders)
Notes: Let’s have a look at the steps needed to perform a multiplication operation and see how this going to be mapped to an FPGA. First partial products are generated which is an AND operation between two bits, one from each operand. Then those partial products are added together to generate the final products. This addition is done one 1 or more steps depending on the multiplication size.

## Slide 11: Stratix-10: Unsigned 4-bit Multiplier Mapping
ALM Count: 10
Geomean: 25.0 ALMs
(4-bit to 9-bit multipliers)
Notes: This animation will show how a 4-bit unsigned multiplier is mapped to the stratix-10 logic block. An unsigned multiplier is chosen for easier illustration. However, for signed multiplier its almost the same mapping. First the partial products are generated using the 4-input LUTs are directly added together using the adder chain in front of the LUTs. Then the outputs are added again together to produce the final product. As shown, 10 ALMs are needed to map this multiplier. Since we are concerned with low-precisions. We studied the mapping of 4-bit to 9-bit multiplications which have a geometric average of 25 ALMs

## Slide 12: Stratix-10: Perfect Resource Utilization?
Observations:
LUTs used as buffers for adder inputs
4-LUT implementing 2-input AND
2
1
Notes: First we can see that in some ALMs the LUTs are being used to pass inputs to the FAs which underutilizes the LUTs.
Second, for partial product generation 4-LUTs are underutilized as they are used as 2-LUTs.
Third, Some ALMs are only used to generate the Cout signal which wastes the ALM resources.

## Slide 13: Proposed Architectures
Notes: Given the observations we have mentioned in the previous slide. We are going to propose architecture changes that can solve one or more the causes for the under utilization observed.

## Slide 14: Design Constraints
Backward compatibility (functionality)
  Should support all the operations of the baseline architecture
Low added cost (area/delay)
  Modifications shouldn’t negatively affect the general purpose nature of the FGPA
Same routing architecture (routing interfaces)
  Should preserve current I/O interfaces of LAB and ALM
Notes: The new logic block design should be backward compatible meaning it should be able to support all the operations the baseline architecture is capable of implementing
The new design should have low area and delay overhead for general applications. Meaning these modifications shouldn’t negatively affect the general purpose nature of the FGPA.
Further, we also added another constraints; which is preserving the current I/O interfaces of the LAB and the ALM. This constraints makes it easy to measure the actual influence of our changes.

## Slide 15: Extra Carry Chain Architecture
Problem:
  LUTs used as buffers for adder inputs
Solution:
  Add a second level of carry chains
Gains:
  Shorter critical path
  Better ALM utilization
1
Notes: We first propose the extra carry chain architecture which is trying to tackle the first observation we found when we looked at the under utilization cause by the current architecture.

## Slide 16: Extra CC: Unsigned 4-bit Multiplier Mapping
ALM count: 7 (vs. 10)
Geomean: 17.3 (vs. 25) ALMs
(4-bit to 9-bit multipliers)
1
One ALM-level less

## Slide 17: Extra CC: Unsigned 4-bit Multiplier Mapping
1

## Slide 18: 4-bit Adder Architecture
Problem:
  4-LUTs used as 2-input LUT
Solutions:
  Fracture 4-LUTs into 3-LUTs
  Generates 8 partial products using the 8 LUTs per ALM (instead of 4)
  Needs extra adders
Gains:
  Fit more adders per ALM
  Better ALM utilization
2
Notes: The result is better alm utilization. Now we generate 8 partial products using the 8 LUTs per ALM instead of 4 and we are able to add those partial products together using the 4 adders we have per ALM

## Slide 19: 4b Adder: Unsigned 4-bit Multiplier Mapping
ALM count: 7 (vs. 10)
Geomean: 15.8 (vs. 25) ALMs
(4-bit to 9-bit multiplier)
2

## Slide 20: Shadow Multiplier Architecture
How to increase area efficiency even more?
Idea: Add a low-precision shadow multiplier per LAB
Shares inputs with ALMs
Steals out ports from ALMs
  If multiplier isn’t used, ALM 8-9 can be used
  Area cost for programmable routing is not wasted for unused hard circuit tiles
3
Notes: Did we just lose flexibility by adding a hard multiplier.

## Slide 21: Recap: Proposed Architectures
1
Extra Carry Chain
2
4-bit Adder
3
Shadow Multiplier

## Slide 22: Extra Carry Chain Architecture
1
Notes: We first propose the extra carry chain architecture which is trying to tackle the first observation we found when we looked at the under utilization cause by the current architecture.

## Slide 23: 4-bit Adder Architecture
2
Notes: The result is better alm utilization. Now we generate 8 partial products using the 8 LUTs per ALM instead of 4 and we are able to add those partial products together using the 4 adders we have per ALM

## Slide 24: Summary
Low-precision can increase DNN efficiency
FPGA logic blocks can implement efficient MACs
Extra CC: 1.5x MAC density for only +2.6% tile area
4b Adder: 1.6x MAC density for only +2.9% tile area
SM: up to 4.1x MAC density for up to +14.8% tile area
SM + 4b Adder: up to 6.1x MAC density for up to +16.7% tile area
Notes: Results show that the extra carry chain architecture could increase the MAC density by 1.5x while having insignificant impact on area and delay.
Modified COFFE to support state-of-the-art Stratix 10 LB architecture
Proposed three logic block architectures that can increase the MAC density on the FPGA’s soft logic
Showed that architecture changes with low costs can lead to significant gains in reducing MAC areas.