## Slide 1: Coarse-Grained Reconfigurable Devices (CGRA)

## Slide 2: CGRA - Introduction
CGRA:
  Array of operation units + memories + routing resources
  Functional units:
    Customized for specific application/domain
    Acceleration of Convolutional neural networks (application), machine learning (domain)

## Slide 3: CGRA - Introduction
Closer look
[Karunaratne17]

## Slide 4: CGRA - Introduction
CGRA vs. FPGA:
  FPGA:
    Boolean-level blocks
    Mainly bit-width operations (LUT/MUX)
  CGRA:
    Computational blocks
    Word-width operations

## Slide 5: CGRA - Introduction
Advantages:
  Better performance per power (for computation-centric applications)
  More efficient area usage for interconnections
    In FPGAs: major portion of config. info.: for routing resources
    In CGRA: interconnections bundled to words with fewer config. bits.
  Less CAD complexity
    Due to reduced number of decisions
  Easier dynamic reconfiguration (fast context switching)
Disadvantages:
  Less general purpose
    CGRAs are mostly research prototypes

## Slide 6: CGRA as Accelerator/Coprocessor
Two types:
  Stand-alone
    Should be able to execute the entire application
  Mainly as accelerator to processors:
    Computation-intensive part  CGRA
      CGRA components: similar to components of processors
    Host:
      RISC
      VLIW: Advantage: speed up the software part of application (Amdahl’s law)

## Slide 7: Hardware Platforms for Coarse-Grained Applications
[Liu19]

## Slide 8: Hardware Platforms for Coarse-Grained Applications
[Liu19]

## Slide 9: Applications
Security
  Reconfigurable cryptographic processors for multiple algorithms
    COBRA (for > 40 symmetric ciphers)
    Celator (for block ciphers (AES/DES) and hash functions (SHA))
    Cryptoraptor (for symmetric key cryptography)

## Slide 10: Applications
Signal and image processing
    Advanced video coding (H.264/AVC) or MPEG4
    Image processing
    Networks: Software defined radio, MIMO detection

## Slide 11: Applications
Deep learning
    Eyeriss (MIT):
    Convolutional neural networks (CNN) operations in systolic manner
    Reconfigurable hybrid-neural network processor for deep learning application
Biomedical Engineering
    Samsung SRP: Mobile healthcare
Mobile Computing:
    In Samsung Exynos processor

## Slide 12: ADRES

## Slide 13: ADRES
ADRES (Architecture for Dynamically Reconfigurable Embedded System) [Mei03]
  Couples VLIW and CGRA (2 modes of operation)
  Resource sharing (FUs and RFs)
FU: Functional Unit
RF: Register File
RC: Reconfigurable Cell

## Slide 14: ADRES
FUs:
  Execute word-level operations (selected by a control signal)
RFs:
  Store intermediate data
Resource sharing for two views:
  Don’t execute simultaneously
Communications between two parts:
  Through shared RFs

## Slide 15: ADRES
Reconfigurable Cell (RC):
  Configuration RAM:
    Can store a few configurations
    Loaded at each cycle to SRAM cells
      Reconfigured at each cycle in CGRA mode
    Like instruction execution:
      Configuration determines the behavior of cell by selecting operations and muxes
Purpose of reconfigurable matrix:
  Accelerate dataflow-like operations in parallel

## Slide 16: ADRES
Template architecture:
  Detailed architecture: XML-based language:
    Communication topology
    Operation set
    Timing of target architecture
    Shared resources:
      E.g., two FUs share one RF

## Slide 17: Samsung ULP-SRP

## Slide 18: Samsung SRP
ULP-SRP (Ultra Low Power - Samsung Reconfigurable Processor) [Kim14]:
  For mobile healthcare device
  Based on ADRES
    VLIW mode
    CGRA mode
  Aims:
    High performance (parallel FUs)
    Low energy
  CGRA mode:
    Many FUs working in parallel
    Increased power consumption but shortening the execution time
    Positive effect of shorter run time > Negative effect of power consumption
       better energy efficiency

## Slide 19: Samsung SRP: Die Photo

## Slide 20: SRP Architecture
VLIW mode:
  For complex processing that cannot be scheduled on CGRA
CGRA LP mode:
  Low performance
    Sufficient for some biomed. applications
CGRA HP mode:
  High performance
    For more complex algorithms

## Slide 21: Loop Scheduling
Software pipelining for loops:
  Scheduling of loops
    Considering DFG
    Using 2 parallel FUs (FU0, FU1)
Data Flow Graph
T = 7
T = 8

## Slide 22: Loop Scheduling
Software pipelining for loops:
  Scheduling of loops
    Loop pipelining
Data Flow Graph

## Slide 23: SRP Mode Selection
Dynamic mode selection:
  Some loops have high data parallelism
     High Instruction Per Cycle (IPC)
     Run in HP mode
  Some loops don’t
     low IPC
     Run in LP mode  low energy
  Compile application twice:
    Performance simulator  execution cycle of each loop for two modes
     Uses mode selection for each loop

## Slide 24: SRP Mode Selection

## Slide 25: SRP Mode Selection
ECG application
FFT application
  high data parallelism and IPC of FFT
   HP: energy-efficient for the entire loop

## Slide 26: SRP Mode Selection
Duty cycle in ECG application
  Tprocess / (Tprocess + Tdata collection)
  HP mode  smaller(?) duty cycle

## Slide 27: SRP Mode Selection
EMG application (ElectroMyoGram)
  Collects electrical activity from muscles
Execution cycles of each loop mapped to CGRA (threshold: 1.7)

## Slide 28: SRP Mode Selection
EMG application
  Dynamic mode selection:
    Combination of modes

## Slide 29: Unified Memory Architecture
Reconfigurable memory
  Some applications need more data (instruction) memory than others
    A 3-channel ECG application needs 3× bigger data buffer than 1-channel ECG
Notes: Data address (instruction address) is decoded and lets the data be written/read to the appropriate address in shared memory or data memory. E.g., shared memory is specified for data. Then when data address is decoded, the address causes the DEMUX to send the write data to either shared memory or data memory (depending on the address value). Or the decoded address causes the MUX to get the data from either the shared memory or data memory to Read Data. In fact the output of Address Decoding module should be connected to the top and bottom MUXes as well. And Inst. Address and Data Address (lower significant bits) should be connected to the memory blocks too.

## Slide 30: HyCUBE

## Slide 31: HyCUBE
CGRA with configurable interconnect architecture
   Single-cycle communications between distant FUs
    Most CGRAs: static links connecting neighbor to neighbor
     Distant FUs: routed through intermediate FUs
     Costs: Multiple cycles + Occupied FUs
  Previous analysis (ADRES):
    Optimal energy-efficiency can be achieved through addition of more interconnects

## Slide 32: Conventional CGRA
Neighbor-to-neighbor:
  If neighboring PEs are not available, dependent operations are mapped farther apart:
    Must traverse farther
     More cycles
 HyCUBE:
  communicates with distant PEs in a single cycle
+
X
-
+
X
-
MORE CYCLES
R
R
SINGLE CYCLE

## Slide 33: HyCUBE Architecture
CGRA with configurable interconnect architecture
Crossbar Switch:
  6 inputs to 7 outputs
Multicasting
7
0
X
1
X
4
X
5
X
2
X
3
X
6
X
X
8
X
9
X
12
X
13
X
10
X
11
X
14
X
15
X
D A T A M E M O R Y
CrossBar Switch
NORTH
EAST
NORTH
R0
EAST
WEST
SOUTH
R1
R2
R3
WEST
SOUTH
ALU
CONFIG
MEM
P
OP
XBAR
Asynchronous Repeaters
I 1
I 2
RES

## Slide 34: Optimal Mapping (N2N CGRA)
F0
F1
F2
F3
N1
N2
N3
N4
N5
N7
N6
DFG of an loop iteration
2x2 CGRA
F0
F1
F2
F3
F0
F1
F2
F3
F0
F1
F2
F3
F0
F1
F2
F3
N1
N3
N2
R
N4
N5
R
N6
N1
N6
CYC 0 / CYC 3
CYC 1
CYC 2
CYC 3/ CYC 0
N1
N4
N5
N1
R
N4
N5
N3
N6
N3
R
N6
N7

## Slide 35: Mapping Example (N2N CGRA)
Mapping example:
DFG
2x2 N2N CGRA architecture
Another view

## Slide 36: HyCUBE
Optimal mapping on N2N:
-

## Slide 37: Optimal Mapping (HyCUBE)
Advantage:
  Any FU can reach far-away FU (or multiple FUs): within a single cycle
N1
N2
N3
N4
N5
N7
N6
N1
N5
F0
N1
F1
F0
F1
F2
F3
F0
F2
F3
F1
F2
F3
N1
N2
N3
N4
N5
N6
N7
N6
N7
N1
N5
CYC 0 / CYC 2
CYC 1
CYC 0 / CYC 2
Initiation Interval (II) = 2:
  Number of cycles between the initiation of two consecutive loop iterations

## Slide 38: HyCUBE
Optimal mapping on HuCUBE:
  Any FU can reach far-away FU (or multiple FUs) within a single cycle
Initiation Interval (II):
  Number of cycles between the initiation of two consecutive loop iterations

## Slide 39: HyCUBE
Comparison with commercial devices

## Slide 40: HyCUBE RTL Implementation
4x4 CGRA synthesized + P&R
Power estimates via RTL Simulation
Technology | TSMC 28nm
Max. Freq | 704 MHz
Area | 0.64 mm2
Power | 115.60 mW
 | Perf(MIPS) | Power(mW) | MIPS/mW
ARM Cortex-A5 | 2229 | 143 | 16
Xilinx Artix7 | 22604 | 1410 | 17
Samsung RP | 467 | 21 | 32
HyCUBE | 6648 | 105 | 63
Performance and Power (Scaled to 28nm) for running 256-FFT
  Artix 7 FPGA: 10x faster than ARM
  SRP: 2x better power efficiency than ARM but much slower
  HyCUBE: 3x faster and 4x more power efficient than ARM
Notes: As for the HyCUBE’s RTL implementation we used a 4x4 version on TSMC 28nm.
We evaluated HyCUBE against the other processing architectures suitable for embedded domain and it turns out HyCUBE brings the best power-efficiency.

## Slide 41: Clustered Architecture

## Slide 42: Clustered Architecture
Clustered architecture [Walker19]:
  Groups of 4 PEs connected to crossbars connected in a grid
  PEs within a cluster: fully-connected
    Only one connection between clusters
  Each cluster:
    One memory port
    One IO port

## Slide 43: References
Motomura, Hariyama and Watanabe, “Advanced Devices and Architectures,” in Hideharu Amano, Principles and Structures of FPGAs, Springer, Singapore, 2018.
Mai, et al., “ADRES- An architecture with tightly coupled VLIW processor and coarse-grained reconfigurable matrix,” FPL, 2003.
Kim, et al., “ULP-SRP: Ultra Low-Power Samsung Reconfigurable Processor for Biomedical Applications,” ACM Transactions on Reconfigurable Technology and Systems, Vol. 7, No. 3, August 2014.
Karunaratne, et al., “HyCUBE: A CGRA with Reconfigurable Single-cycle Multi-hop Interconnect,” DAC 2017, USA.
Walker and Anderson, “Generic Connectivity-Based CGRA Mapping via Integer Linear Programming,” 2019

## Slide 44: References
Liu, Leibo, Jianfeng Zhu, Zhaoshi Li, Yanan Lu, Yangdong Deng, Jie Han, Shouyi Yin, and Shaojun Wei. "A survey of coarse-grained reconfigurable architecture and design: Taxonomy, challenges, and applications." ACM Computing Surveys (CSUR) 52, no. 6 (2019): 1-39.
Podobas, Artur, Kentaro Sano, and Satoshi Matsuoka. "A survey on coarse-grained reconfigurable architectures from a performance perspective." IEEE Access 8 (2020): 146719-146743.