## Slide 1: Reconfigurable Systems: Applications

## Slide 2: Applications
For speed-up
For power-efficiency
For reconfigurability

## Slide 3: Reconfigurable Systems Advantages
Performance enhancement
  Performance enhancement through scaling stopped
    Architectures with highly parallel structures can fill the gap.

## Slide 4: Speedups (repeated)
Reported speedups:
  Up to x28500

## Slide 5: Speedups (repeated)
SR: Super-Resolution:
  Construction of high-resolution images from several low-resolution observations
  Speedup: up to 4 orders of magnitude
[Georgis16]

## Slide 6: Speedups
Password guess:
  Pico-FPGA board:
    Xilinx Virtex-6 FPGA
  i7-920:
    Intel CPU
  AMD Radeon:
    AMD GPU
  NVIDIA GTX 480
    GPU
[ExtremeTech12]

## Slide 7: Speedups
Source: "The Evolution of Bitcoin Hardware" by Michael Bedford Taylor (University of Washington), CoinDesk Research

## Slide 8: Speedups
Cryptocurrency mining:
  Throuput and energy efficiency
[iSilicon16]

## Slide 9: High-Performance Computing (HPC)
TOP500/Green500
  Ranking of the 500 fastest and energy-efficient supercomputers since 1986/2007
    Green500: Power-performance

## Slide 10: HPC
HA-PACS:
  University of Tsukuba
  8th generation: adopted GPUs as computational nodes
  GPUs could not share the data efficiently
  Uses Stratix FPGA
  164th place at the TOP500, 3rd place at the Green500

## Slide 11: FPGA as a Network Chip
  Difficult to increase the transceiver speed at the same pace as before in the next decade.
  Must increase number of transceivers per FPGA

## Slide 12: FPGA as a Network Chip
Network companies with network products with FPGA:
  Exablaze
  Arista
  Cisco
  Mellanox
  Simplex

## Slide 13: Big Data: Web Search
Web search engines:
  Scan huge databases to find the Web pages containing keyword(s)
  Web pages are scored and sorted in terms of their relevance with the keyword.
Past:
  Built on PC-based server clusters
Present:
  Large-scale data centers facing power wall
   FPGA

## Slide 14: Microsoft Bing Search Engine
Search procedure:
  Queries (search terms)  servers  IFMs (Index File Managers)
  Each IFM performs rank calculation on ~10,000–20,000 documents.
  Results  servers  front-end
IFM:
  Document score calculation: computation-intensive
   FPGA-based accelerator

## Slide 15: Microsoft Bing Search Engine
Score Calculation:
  Feature extraction: many custom FSMs in FPGA
    Software: 600 µs
    FPGA: 4 µs
  Machine learning scoring (MLS): final score calculation
    Algorithm is frequently updated
     Reconfigurability of FPGA
FPGA:
  8 Stratix-based boards
FPGAs in Microsoft's Intelligent Cloud Computing

## Slide 16: Bioinformatics: Genomics
Genome:
  String of DNA molecules of size ~109 for human
    A (adenine)
    T (thymine)
    C (cytosine)
    G (guanine)

## Slide 17: Bioinformatics: Genomics
Genome analysis:
  String processing algorithms
  Acceleration by custom FSMs in FPGA
  Data words: 2 bits
     more suitable for FPGA (than CPU/GPU)

## Slide 18: Genome Assembly from Short Reads
De Novo Genome assembly:
  Read a massive number of short fragments of DNA (reads)
  From short reads, Find overlaps on both ends
  Construct the genome
    No reference sequence used

## Slide 19: Short Read Mapping on a Reference Genome
Human genome:
  Everyone have a slightly different genome sequence
    Differences:  medical interests (potential diseases, …)
Obtaining personal genome sequence:
  By mapping DNA reads to reference human genome sequence
FPGA:
  Massively parallel mapping

## Slide 20: Deep Learning
Microsoft Azure Project:
  Accelerated Machine Learning with Project Brainwave
  Uses Intel FPGA
Video: Azure Accelerated Machine Learning with Project Brainwave

## Slide 21: Power Efficiency
Power Consumption:
  As a global issue
  Power wall in chips

## Slide 22: Power/Energy as a Global Issue
Energy consumption (if current rate):
  By the year 2030, x30 growth only for ICT (Information and Communication Technology)
  >> current total energy consumption for everything
More growth because of:
  More Internet users
  More IoT things
  More social networks
  More video on demand
  More cloud computing
  More electronic books
  …

## Slide 23: Power/Energy as a Global Issue
Greenhouse gas emission:
  Currently higher than total air traffic
Electricity bill for data centers:
  Google: Currently higher cost than its equipment
  Soon: cost of a data center solely by monthly power bill
    Google’s water-based data centers (on the ocean)

## Slide 24: Cooling in Data Centers

## Slide 25: Google’s Floating Data Center

## Slide 26: Power/Energy as a Global Issue
Limited oil production:
  Peak production reached in 2009
Conclusion:
  Computing performance: MIPS/W (not just MIPS)

## Slide 27: Future High-Speed Systems
Power wall:
  Frequency scaling:
    20% to 30% per year
  Supply voltage scaling (to keep power low):
    -15% per tech. generation
    Recent years: slowed down
       Approaching power wall:
        Max power that can be dissipated for a given chip area (~90 W/cm2)
  No increase in frequency: not useful (static power)
Solution:
  Dark silicon:
    Keep parts of the chip off

## Slide 28: Power Wall in Chips
Power wall:
  Supply voltage does not scale as before (15% per year)
     Power consumption is approaching its ultimate limit:
      that can dissipate for a given chip area (~90 W/cm2)
     Need to limit activity of transistors
      Not sufficient due to static power
[Kaeli15]

## Slide 29: Power Wall in Chips (repeated)
Power wall:
  Percentage of a microprocessor chip that can be ON (to keep within the available power budget)
[Kanduri17]

## Slide 30: Power Wall in Chips
Limitation on available gate-density:
  Future chips: more resources than what can be powered ON at any given time.
Efficient solution:
  Heterogeneous architecture:
    Most efficient core/module will be chosen dynamically for an application/task at hand.
     Dynamic (on-demand) resource allocation in reconfigurable systems:
    Install at a post-fabrication phase the most suitable core/accelerator for a certain task (rather than predicting at design time the most efficient architecture).

## Slide 31: Future High-Speed Systems
Power wall:
  Future chips: more resources than what can be powered ON at any given time.
  Resource overhead of reconfigurable device NOT a limiting factor:
   Extra area offer reconfigurability (flexibility) targeting:
    reliability
    performance enhancement

## Slide 32: Applications for Reconfigurability

## Slide 33: Reliability
Technology trend:
  Shrinking feature size 
    Less reliable transistors
    Too many devices defective at manufacture time
    Many devices fail over time (e.g., by aging)
    More soft errors

## Slide 34: Reconfigurable Systems Advantages
Reliability
  Reconfigurable devices: excellent for fault tolerance:
    Adapt to new faults on demand (e.g., aging)
    Isolate defects
    Correct defects
    Provide spare resources to substitute defective blocks

## Slide 35: Rapid prototyping
Verifying ASIC in real conditions before fabrication
    High NRE costs
  Software simulation
    Relatively inexpensive
    Slow
    Accuracy?
  Hardware emulation
    Hardware testing under real operation conditions
    Fast
       Allows many more iterations
    Accurate

## Slide 36: Cadence Palladium
hardware/software co-verification
Features:
  Up to 1,000,000X faster than RTL simulation
  Maximum capacity of up to 256M ASIC gates
  Debug time:
    from months to hours
Notes: In terms of throughput (Hz): Number of test vectors per second

## Slide 37: Cadence Protium X2
Protium X2
  Xilinx UltraScale+
  10 B gates in 10 hours

## Slide 38: Post Fabrication Customization (repeated)
Manufacturer
Time to market advantage
  Ship the first version of a product
Remote upgrading with new product versions
Remote repairing

## Slide 39: Adaptive Computing Systems
Uncertainty and unpredictability of some systems:
   impossible, at compile time, to address all scenarios that can happen at run-time.

## Slide 40: Adaptive Computing Systems
Adaptive computing systems:
  Computing systems that are able to adapt their behaviour and structure to
    changing operating and environmental conditions
    time-varying optimization objectives,
    physical constraints
      e.g. changing protocols, new standards
Example:
  Mars rover vehicle:
    Some FPGAs can be modified from the earth.

## Slide 41: References
  Hideharu Amano, Principles and Structures of FPGAs, Springer, Singapore, 2018.
  João M. P. Cardoso, Michael Hübner (eds.), Reconfigurable Computing: From FPGAs to Hardware-Software Codesign, Springer, New York, 2011.
  Microsoft Co. (2019, April 8, Project Catapult, [Online]. Available:https://www.microsoft.com/en-us/research/project/project-catapult/#!videos
  [Kaeli15] Kaeli, et al, Heterogeneous Computing with OpenCL 2.0, Morgan Kaufmann, 2015.
  [Georgis16] Georgis, Georgios, George Lentaris, and Dionysios Reisis. "Acceleration techniques and evaluation on multi-core CPU, GPU and FPGA for image processing and super-resolution." Journal of Real-Time Image Processing (2016): 1-28.
  [ExtermeTech16] Joel Hruska, “Intel launches Stratix 10: Altera FPGA combined with ARM CPU, 14nm manufacturing,” ExtremeTech, 2016.

## Slide 42: References
  Kanduri, Anil, Amir M. Rahmani, Pasi Liljeberg, Ahmed Hemani, Axel Jantsch, and Hannu Tenhunen. "A perspective on dark silicon." In The Dark Side of Silicon, pp. 3-20. Springer, Cham, 2017.