## Slide 1: Routing Architectures

## Slide 2: Connection Blocks and Switch Blocks
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block

## Slide 3: Global vs. Detailed Routing View
Global (macroscopic) view:
  Relative position of routing channels in relation to the positioning of logic blocks
  How each channel connects to other channels
  # of wires in each channel
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block

## Slide 4: Global vs. Detailed Routing View
Detailed (microscopic) view:
  Lengths of the wires,
  Specific switching quantity and patterns between and among wires and logic block pins
  Single-driver vs. multiple-driver wires
     wires that send signals in a specific direction
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block

## Slide 5: Global Routing Architecture
Global Routing Architectures:
  Island-style
  Hierarchical

## Slide 6: Island-Style Architecture
Island-Style:
  Logic blocks arranged in a 2D mesh with routing resources evenly distributed
  Has routing channels on all four sides of the logic blocks
  W: # of wires contained in a channel
    pre-set during fabrication
    one of the key choices made by the architect

## Slide 7: Island-Style Global Routing

## Slide 8: Connection Blocks and Switch Blocks
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block
LB
Connection
Block
Switch
Block

## Slide 9: Connection Architecture

## Slide 10: Programmable Switch Matrix (PSM)

## Slide 11: Field Programmable Gate Array (FPGA)

## Slide 12: Global Routing Architecture
Hierarchical Architecture:
  Logic blocks clustered in groups hierarchically
  Connections between logic blocks within a group by wire segments at the lowest level
  Connections between logic blocks in distant groups: traversal of one or more levels
    Wider routing channels at levels furthest from the logic blocks
      Like Freeways vs. streets

## Slide 13: معماری اتصالات سلسله‌مراتبی
  اتصال یک بلوک به بلوک دیگر:
    عبور از حداکثر سه سطح سوییچ
  ابزار جایابی LBهای متصل را در یک خوشه قرار می‌دهد
LB1.1.1
LB1.1.2
LB1.1
LB1.2
LB1
LB1.2.1
LB1.2.2
LB2.1.1
LB2.1.2
LB2.1
LB2.2
LB2
LB2.2.1
LB2.2.2
LB3.1.1
LB3.1.2
LB3.1
LB3.2
LB3
LB3.2.1
LB3.2.2
LB4.1.1
LB4.1.2
LB4.1
LB4.2
LB4.2.1
LB4.2.2
LB4

## Slide 14: معماری اتصالات سلسله‌مراتبی
LB1.1.1
LB1.1.2
LB1.1
LB1.2
LB1
LB1.2.1
LB1.2.2
LB2.1.1
LB2.1.2
LB2.1
LB2.2
LB2
LB2.2.1
LB2.2.2
LB3.1.1
LB3.1.2
LB3.1
LB3.2
LB3
LB3.2.1
LB3.2.2
LB4.1.1
LB4.1.2
LB4.1
LB4.2
LB4.2.1
LB4.2.2
LB4
LB
LB1
LB1.1
LB1.2.1
LB2
LB2.1
LB3
LB3.1
LB3.2
LB4
LB4.1
LB4.1.1
LB1.2
LB1.1.1
LB1.1.2
LB1.2.2
LB2.1.1
LB2.1.2
LB3.1.1
LB3.1.2
LB3.2.1
LB2.2
LB2.2.1
LB2.2.2
LB3.2.2
LB4.1.2
LB4.2
LB4.2.1
LB4.2.2

## Slide 15: Hierarchical Routing Architecture
Advantages:
  More predictable inter-logic block delay following design placement
    If interconnect delay is not significant, maximum delay is almost equal for all connections.
  Superior performance for some logic designs
Disadvantages:
  Each level of the hierarchy: a hard boundary
    Once traversed  significant delay penalty
    Physically close logic blocks but apart with respect to the hierarchy
  In newer technologies, significant wire delay
     Many recent commercial FPGAs: Two or three levels of hierarchy

## Slide 16: Island-Style Architectures
Commercial FPGAs: Island-style with 2-level hierarchy (most new devices):
  Lattice LatticeXP
  Xilinx Spartan & Virtex family
  Intel Stratix & Cyclone family

## Slide 17: Intel Cyclone
M9K
Memory
M9K
Memory

## Slide 18: Intel Cyclone

## Slide 19: Spartan CLB

## Slide 20: معماری اتصالات

## Slide 21: Connection Block
Fc,in
  Input connection block flexibility
Fc,out
  Output connection block flexibility

## Slide 22: Connection Block
Fc,in
  Input connection block flexibility
Fc,out
  Output connection block flexibility

## Slide 23: Switch Block
Switch Blocks:
  Form connections between wire segments at intersections of a horizontal and vertical channel.
Fs:
  Switch block flexibility:
    # of possible connections a wire segment can make to other wire segments
    Fs = ?

## Slide 24: Programmable Switch Matrix (PSM)

## Slide 25: Disjoint vs. Wilton Switch Blocks
Disjoint:
  A wire entering a disjoint switch block to other wires with the same number
     Potential source–destination routes: isolated into distinct routing domains
     limiting routing flexibility.

## Slide 26: Disjoint vs. Wilton Switch Blocks
Wilton:
  Uses the same number of routing switches
  overcoming domain issue  can change domain
    Greater diversity of routing paths from a net source to a destination

## Slide 27: Multiple Block Length Wire Segments
A wire runs for L logic blocks:
LB
LB
LB
LB
L=2
L=3
switch
L=1
switch
switch
switch
switch
switch
switch

## Slide 28: Multiple Block Length Wire Segments
Example:
  40% of tracks: length 1
  40%: length 2
  20%: length 4

## Slide 29: Routing Switches
Bidirectional switches:
  Pass transistors:
    Less area
    Fast for short wiring paths (passing through a small number of switches)
  Buffers:
    Faster for connections passing through many switches
 Mixed PT and tri-state buffers:
  better delay characteristics with the same area

## Slide 30: Unidirectional Switches
Bidirectional wire segments:
  Can be driven by switch blocks on both ends.
  [Lemieux04]: Once programmed, leaves 50% of switches inactive (unused)
  Extra sinks  more capacitance  delay
Directional wire segments:
  [Lemieux04]: halves the required tri-state buffers per switch

## Slide 31: Unidirectional Switch Options
Directional tri-state (dir-tri):
  Multiple driver:
  Each wire segment is driven by:
    adjacent wire segments
    one or more LB output pins (via a PT)

## Slide 32: Unidirectional Switch Options
Single-driver:
  A multiplexer selects inputs from both wire segment and logic block sources.
  Each wire segment can be driven by a non-tri-state buffer
    Improved drive strength
  100% single-driver always gave the best results for area and delay.

## Slide 33: Research in Routing Architecture Design

## Slide 34: More Recent Routing Improvements
HARP: Hardwired Routing Patterns [Wang06]:
  Junction patterns: L, T, +

## Slide 35: HARP Patterns
Some hard-wired patterns

## Slide 36: Routing Graphs
  In Virtex 5, diagonal wires are used

## Slide 37: HARP Research Procedure
Routing requirement analysis:
  A number of circuits were placed and routed on traditional FPGA architectures,
  Routing patterns that were formed in the switch boxes are analyzed.
HARP architecture generation:
  Based on the frequencies of the patterns, HARP patterns were instantiated and replaced some switches.
Placement and routing with HARPs:
  Place and route circuits on the new HARP architecture.

## Slide 38: Performance Scaling
Effect of architectural innovations on performance:
  Longer wires span multiple logic blocks
   Making distant logic closer
[Trimberger15]
  HARP
  Double/quad-length
  2-level hierarchy

## Slide 39: Power Consumption

## Slide 40: Power Consumption
Power Consumption:
  Dynamic Power:
    Pd = k.CL.Vdd2.f
  Leakage Power:
    Much of the interconnect resources within the FPGA are not actively used.
  60%–70% of FPGA dynamic and static power consumption: in programmable interconnect

## Slide 41: Power Consumption
Power Consumption:
  Dynamic Power:
    Pd = k.CL.Vdd2.f
  Leakage Power:
    Much of the interconnect resources within the FPGA are not actively used.
    Components:
      Source-to-drain subthreshold leakage
      Gate-to-source gate oxide leakage
  60%–70% of FPGA dynamic and static power consumption is located in the programmable interconnect.

## Slide 42: Leakage Power
Power Consumption:
  Leakage Power

## Slide 43: Sub-threshold Current
  At Vgs = Vt (and a little before), Ids > 0 (sunthreshold region)
    Must reduce Vgs still more to cut-off the channel
  Isub ≈ 10-10 A @ Vgs = 0
  Isub ≈ 10-5 A @ Vgs = Vt
    increases exponentially

## Slide 44: Gate Oxide Leakage
Gate oxide leakage:
  Electron tunneling as the transistor gate oxide is thinned
     Leakage current increase exponentially with oxide thinning

## Slide 45: Leakage Power
Reason for increase in Leakage:
  Vdd: reduced with scaling
  Vth must be lowered to recover switching speed
     Subthreshold leakage current increases exponentially
  Oxide thinning continued

## Slide 46: Power Reduction
Power reduction techniques in general:
  Removing VDD from unused transistors:
     Leakage power reduction
  Reduce VDD for some transistors:
     Dynamic power reduced a lot
Multi-supply voltage (MSV) :
  high voltage on critical paths to maintain performance
  low voltage on non-critical paths to reduce power

## Slide 47: Power Reduction in FPGA
Power reduction techniques in FPGAs:
  Drive each routing buffer by two separate sources [Li04]:
    A full-rail VDD (VDDH)
    A reduced VDD (VDDL).
   3 cases:
    high-performance (M1 active),
    reduced performance (M2 active),
    sleep mode (both shut off)

## Slide 48: Power Reduction in FPGA
  Experiments:
    88% of interconnect buffers could be placed into sleep mode
    85% of active routing buffers could be driven with VDDL without increasing circuit delay.
     80% overall reduction in interconnect leakage
    38% reduction in interconnect dynamic power

## Slide 49: Power Reduction in FPGA
Problem:
  requires the chip-wide distribution of multiple VDD values
Solution:
  VDD-selection approach for routing buffers [Anderson04]
  3 cases:
    SLEEP = ‘1’, LOWPOWER = ‘0’
    SLEEP = ‘0’; LOWPOWER = ‘1
    SLEEP = ‘0’, LOWPOWER = ‘0’

## Slide 50: Power Reduction in FPGA
Problem:
  requires the chip-wide distribution of multiple VDD values
Solution:
  VDD-selection approach for routing buffers [Anderson04]
  3 cases:
    SLEEP = ‘1’, LOWPOWER = ‘0’
      Both off  sleep mode
    SLEEP = ‘0’; LOWPOWER = ‘1
      MNX on:
      VVD = VDD – Vt
       Weak supply
       Low power mode
    SLEEP = ‘0’, LOWPOWER = ‘0’
      Both on:
      VVD = VDD
       Buffer in high-performance mode

## Slide 51: Power Reduction in FPGA
Experiments:
  75% of routing resources could tolerate a slowdown of 50% (70 nm process)
   Leakage power reduction (including effects of the new transistors): about 35%
    when operating in low-power mode (i.e., MPX off, MNX on)
  Area increase: ~ 10%

## Slide 52: MTCMOS in FPGAs
Dual Threshold Technique
  Use low threshold transistor along critical paths
     Optimize performance
  Use high threshold transistor along non-critical paths
    Minimize leakage
[Gayasen04],[Li04]
  High Vt transistors to implement configuration SRAM bits
    Not subsequently read
       Performance: not an issue.

## Slide 53: Power Reduction in FPGA
Body biasing for unused interconnect transistors:
   Adaptive Vt
   Reduce sub-threshold leakage
Disadvantages:
  Needs multi-well process  area
  Needs a circuit to control bias voltages
  Experiments [Rahman04]:
    Area increase: 1.6X to 2X,
    Leakage current reduction: 1.7X to 2.5X

## Slide 54: Power Reduction in FPGA
In commercial FPGAs:
  High Vt transistors for configuration SRAM bits
  Thicker oxides to reduce the leakage of the devices which are not performance critical
    Xilinx, “Power consumption in 65 nm FPGAs, Xilinx White Paper WP246 (v1.2),”http://www.xilinx.com/support/documentation/white papers/wp246.pdf, February 2007.
    Altera Corporation, “Stratix III FPGAs vs. Xilinx Virtex-5 devices: Architecture and performance comparison, Altera White Paper WP-01007-2.1,”http://www.altera.com/literature/wp/wp-01007.pdf, October 2007.

## Slide 55: Power Reduction in FPGA
In commercial FPGAs:
  Speed/power grades:
  Kintex Ultrascale:
    Grade -1, -1L:
      lowest power, lowest speed
      Can both work with 0.95 v
      Grade -1: can work with 0.9 v
    Grade -2, -3:
      High performance (-3 highest)

## Slide 56: References
م. صاحب‌الزمانی، طراحی کامپیوتری سیستم‌های دیجیتال، نشر شیخ بهایی، 1398
[Kuon07] I. Kuon, R. Tessier, “FPGA Architecture: Survey and Challenges,” Foundations and Trends in Electronic Design Automation, Vol. 2, No. 2 (2007) 135–253.
[Xilinx/AMD] www.xilinx.com – www.amd.com
[Altera/Intel] www.altera.com - www.intel.com
[Lemieux04] G. Lemieux, E. Lee, M. Tom, and A. Yu, “Directional and single-driver wires in FPGA interconnect,” in Proceedings: International Conference on Field-Programmable Technology, pp. 41–48, December 2004.
[Wang06] G. Wang, S. Sivaswamy, C. Ababei, K. Bazargan, R. Kastner, and E. Bozorgzadeh, “Statistical Analysis and Design of HARP Routing Pattern FPGAs,” Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), pp. 2088-2102, Vol. 25, No. 10, 2006.

## Slide 57: References
[Li04] F. Li, Y. Lin, and L. He, “Vdd programmability to reduce FPGA interconnect power,” in IEEE/ACM International Conference on Computer Aided Design, 2004.
[Anderson04] J. Anderson and F. Najm, “A novel low-power FPGA routing switch,” in Proceedings of the IEEE Custom Integrated Circuits Conference, pp. 719–722, October 2004.
[Gayasen04] A. Gayasen, K. Lee, N. Vijaykrishnan, M. Kandemir, M. J. Irwin, and T. Tuan, “A dual-VDD low power FPGA architecture,” in Proceedings of the International Conference on Field-Programmable Logic and Applications, pp. 145–157, August 2004.