## Slide 1: Reconfigurable Architectures
Granularity

## Slide 2: Granularity of Reconfigurable Systems
Granularity:
  The abstraction level used to configure the device
  May use a
    Boolean-level,
    instruction-level,
    process-level
    representation.

## Slide 3: Granularity of Reconfigurable Systems
Fine-grain (Boolean-level) architecture:
  FPGA:
    Primary computational elements: limited-input LUTs
  Suitable for simple to complex Boolean functions.
    Inefficient for complex functions like multipliers
Instruction-level:
Process-Level

## Slide 4: Granularity of Reconfigurable Systems
Fine-grain (Boolean-level) architecture:
Instruction-level:
  With computational units that perform instruction-level operations
  Units: byte-width to word-width (32-bit) datapath operations
  Efficient for performing instructions but inefficient at performing Boolean operations.
Process-Level

## Slide 5: Granularity
Fine-grain (Boolean-level) architecture:
Instruction-level:
Process-level:
  Units are complex multi-cycle operations
  Example:
    A cryptography device which decides on the algorithm based on the input key.

## Slide 6: Granularity
Granularity:
  Proportional to the length of a configuration:
    Fine/low-grain: long configuration
    Coarse grain (high-level granularity): short configuration
Efficiency:
  The more closely the application operation is matched to the granularity, the more efficient the device will execute.
Example:
  DSP application needs a lot of word-size add and mult.
     instruction-level granularity
  Application with a lot of Boolean operations:
     Boolean-level granularity

## Slide 7: Hybrid Devices
Recent commercial FPGA devices with multiple levels of granularity:
  LUTs
  Dedicated adders/multipliers
  DSP units
  Microprocessors

## Slide 8: Granularity
  Coarse-grained reconfigurable architectures (CGRA)
  Fine-grained reconfigurable devices (FPGA)
CGRA | FPGA | 
 |  | Terminology
Coarse-grained | Fine-grained | Reconf. granularity
~32 bits | 1 bit | Datapath width
Register-transfer level | Gate level | Physical level of basic units
Adder/Mult/MAC/FP units | LUT, AND/OR/XOR, FF, MUX | Basic units examples
Very fast | Fast | Configuration speed
GHz | ~100 MHz | Clock cycle time
High | Medium | Density

## Slide 9: Area Efficiency
CGRA

## Slide 10: References
  [Hartenstein07] Hartenstein, “Basics of Reconfigurable Computing,” S. P. J. Henkel, Ed. New York: Springer-Verlag, 2007. (updated)
  [Kastner04] Kastner, Kaplan, Sarrafzadeh, “Synthesis techniques and optimizations for reconfigurable systems,” Kluwer, 2004.