## Slide 1: FPGA Technology Mapping

## Slide 2: Research Topic
Choose a topic for presentation
  Oral presentation
  Written report
    Either a research paper or a practical topic
Scehdule:
  Topic selection: 30 Aban
  Oral presentations: 15-17 min.
    29 Azar
    1 Dey
    6 Dey
  Written reports
    6 Dey

## Slide 3: Types of Algorithms
Input to technology mapping:
  Netlist of flip flops
  Nodes with Boolean functions
  [Special-purpose blocks (preserved by synthesis)]
    Multipliers
    Memory blocks
    Adders

## Slide 4: LUT-Technology Mapping
Technology mapping:
  Implements the optimized nodes of the Boolean network to the target device library.
  For FPGA, library elements = LUT
     LUT-based technology mapping (LUT mapping)
Objectives:
    Number of LUTs (area)
    Signal delay (speed)
    Routability
    Power (few publications)

## Slide 5: Types of Algorithms
Classification:
Based on objective functions:
  Area-driven
  Performance-driven
  Routability-driven
  Power-driven
Based on input network:
  Combinational
    Assumes fixed positions for sequential elements
    Only considers the combinational logic between sequential elements
  Sequential
    May relocate FFs during mapping (retiming)
    Can explore a much larger solution space (better quality)

## Slide 6: Types of Algorithms
Structural TM:
  Does not modify the input netlist (except logic duplication).
  Covers a netlist with logic cells (e.g., K-LUTs)
  Efficient for large designs
    Most algorithms are structural.
Functional TM:
  Mixes Boolean optimization with covering
  Can potentially explore a larger solution space than structural mapping
  Time-consuming
     Restricted to small designs (or small portions of a large design)

## Slide 7: FPGAs vs. Custom Logic
Cost metric for custom static gates:
  Literal
    ax + bx’ has four literals: 8 transistors
Cost metric for FPGAs:
  Logic element
    All functions that fit in an LE: same cost

## Slide 8: FPGA Tech Mapping
  Cost (number of inputs) doesn’t always increase with added functions

## Slide 9
LUT-technology mapping problem:
  Covering a Boolean network with a set of K-feasible cones.
    The Boolean network is usually 2-bounded (if not, it is converted to 2-bounded)
Example:
  K = 4
LUT-Technology Mapping

## Slide 10: LUT-Technology Mapping
Graph covering with cones
LUT Mapping
[Chen06]

## Slide 11: LUT-Technology Mapping
LUT-technology mapping problem:
  Covering a Boolean network with a set of K-feasible cones.
Graph covering with cones
LUT Mapping

## Slide 12: LUT-Technology Mapping
Find the largest logic cone that will fit into the LUT:
r = q + s’
q = g’ + h
s = d’
d = a + b

## Slide 13: How much fits in an LUT?
  One 2-input NAND gate frequently used for comparison.
  Approximately 12 ~ 15 gates per 4-input LUT
  20 ~ 30 gates per 6-input LUT
Number of different functions for a 4- input LUT:
  216 functions -> 80 after IO swapping
  14 after IO inversion
A
B
C
D
A
B
C
D

## Slide 14: LUT-Technology Mapping
LUT-technology mapping problem:
  For a combinational logic network, find an equivalent logic network, such that
    each vertex is associated with a function implementable by a LUT.
  Objective:
    Min. # vertices or
    Min. critical path delay