## Slide 1: FPGA Technology Mapping Algorithms
Chortle

## Slide 2: Chortle Algorithm
Chortle [Francis90]:
  Developed by Francis et al, University of Toronto in 1990
  Optimal i.t.o. area
Inputs:
  Fanout-free tree of combinational network
  n-input LUTs
Procedure:
  Dynamic programming:
    Computes and records solutions to all sub-problems proceeding from smallest to largest sub-problem.
      Recording the solution to each sub-problem eliminates the need to recalculate it as part of the solution of any larger sub-problem.

## Slide 3: Dynamic Programming
Example:
  Shortest path problem
    From A to J
    Levelized network:
      A
      B, C, D
      E, F, G
      H, I
      J
[Trick]

## Slide 4: Dynamic Programming
  Shortest distance from node S to the destination J

## Slide 5: Dynamic Programming
  Stage 4:
    F4(H) = 3
    F4(I) = 4
  Stage 3:
3
4
4,H
7,I
6,H

## Slide 6: Dynamic Programming
  Stage 2:
  Stage 1:
3
4
4,H
7,I
6,H
11,E
7,E
8,F

## Slide 7: Chortle Algorithm
Input DAG:
  Assumption: A tree
  If not:
    Convert to a forest of maximal fanout-free tree
n
a
b
c
n
a
b
c
na
nb
nc

## Slide 8: Chortle Algorithm
8
Input DAG:
  Assumption: Fanin of any node <= K
  If > K, then decomposition algorithm:
    Considers all possible decompositions of every node
K = 3
Notes: 8

## Slide 9: Chortle Algorithm
9
Post-Order Tree Traversal
  Visit Left subtree
  Visit Right subtree
  Visit Root
Utilization of LUT at root of subtree (node n):
  The number of inputs, out of K inputs, that are actually used in the circuit.
  U  { 2..K }
  U=K for fully utilized LUT
Minimum Cost of sub-circuit rooted at n
  MinMap(n,Un):
    Optimal solution for node n for U  { 2..K }
[Lockwood06]
Notes: 9

## Slide 10: Chortle Algorithm
10
Utilization Division of an LUT:
  Node n has fanin nodes n1, n2, …, nf
  LUT of n includes all fanin edges of n and some subtrees Si rooted at ni
  Utilization Division:
    Distribution of inputs to the LUT among the subtrees
  U(u1, u2, … uf)
  UD: How the inputs of this LUT are divided among the fanin edges of node n
(1,1,2)
n
n1
n2
nf
Notes: 10

## Slide 11: Chortle Algorithm
Can show:
  For any node n, with fanin nodes n1, …, nf, if we have previously calculated minMap(ni, Ui) for all Ui from 2 to K for every node ni, then we can calculate minMap(n, U) for all U from 2 to K.
n
n1
n2
nf
minMap(n1, 2)
minMap(n1, 3)
minMap(n1, 4)
minMap(n2, 2)
minMap(n2, 3)
minMap(n2, 4)
minMap(nf, 2)
minMap(nf, 3)
minMap(nf, 4)
minMap(n, 2)
minMap(n, 3)
minMap(n, 4)

## Slide 12: Chortle Algorithm
MapTree(T,K)
  For each node (n) in postorder traversal of Tree (T)
    For each utilization (U) = 2 to K of node n {
      CurrentBestCost = ∞
      CurrentBestMap = Ø
      For each Utilization Division (μ (left,right)) such that left+right=U {
        Construct minimum-cost mapping, M, from min maps of fanin nodes computed previously
        Calculate cost (M)
        If Cost (M) < CurrentBestCost (M)
        CurrentBestMap = M
        CurrentBestCost = Cost (M)
        } /* next Utilization Division μ */
      MinMap (n,U) = CurrentBestMap
      } /* next utilization U */
    } /* next node n */
  Return MinMap (root,K)

## Slide 13: Chortle Algorithm
Construct minMap:
  Combine constructed root LUT with the mapping minMap(ni, ui) which have been previously computed
    If ui = 1, minMap(ni,K) must be used instead of minMap(ni, 1)
    The root LUT of minMap(ni, ui) is eliminted because it is within the constructed LUT.

## Slide 14: Chortle: Example
Given:
  F = A*B + (C*D*E) + F
Decompose
  F = (A*B) + (C*D) * E) + F
Given
  K=4
Find Optimal Implementation
  Maptree(n5,2)
  Maptree(n5,3)
  Maptree(n5,4)

## Slide 15: Chortle: Example
For n=n1
  For U=2
    For μn1(1,1)
      CurrentBestMap=n1(A,B)
      CurrentBestCost(M) = 1 LUT
     MinMap(n1,2) = n1(A,B)
      MinCost = 1 LUT
  For U=3 : Same as U=2
     MinMap(n1,3) = MinMap(n1,2)=n1(A,B)
      MinCost = 1 LUT
  For U=4 : Same as U=2
     MinMap(n1,4) = MinMap(n1,2)=n1(A,B)
      MinCost = 1 LUT

## Slide 16: Chortle: Example
For n=n2
  For U=2
    For μn2(1,1)
      CurrentBestMap=n2(C,D)
      CurrentBestCost(M) = 1 LUT
     MinMap(n2,2) = n2(C,D)
      MinCost = 1 LUT
  For U=3 : Same as U=2
     MinMap(n2,3) = MinMap(n2,2)=n2(C,D)
      MinCost = 1 LUT
  For U=4 : Same as U=2
     MinMap(n2,4) = MinMap(n2,2)=n2(C,D)
      MinCost = 1 LUT

## Slide 17: Chortle: Example
For n=n3
  For U=2
    For μn3(1,1)
      CurrentBestMap
      =n3(MinMap(n2,K=4),E)
      =n3(n2(C,D),E)
      CurrentBestCost(M)
      =MinCost(n2) + 1=2 LUTs
     MinMap(n3,2) = n3(n2(C,D),E)
      MinCost = 2 LUTs

## Slide 18: Chortle: Example
For n=n3 (continued)
  For U=3
    For μn3(2,1)
      CurrentBestMap
      =n3(MinMap(n2,2),E)
      =n3(C,D,E)
      CurrentBestCost(M) = 1 LUT
    For: μn3(1,2): Same as μn3(1,1)
     MinMap(n3,3) = n3(C,D,E)
      MinCost = 1 LUT
  For U=4 : Same as U=3

## Slide 19: Chortle: Example
For n=n4
  For U=2
    For μ(left,right)=μ(1,1)
      CurrentBestMap
      =n4(MinMap(n3,K=4),F)
      =n4(n3(C,D,E),F)
      CurrentBestCost(M) = 2 LUTs
       MinMap(n4,2) = n4(n3(C,D,E),F)
        MinCost = 2 LUTs

## Slide 20: Chortle: Example
For n=n4 (continued)
  For U=3
    For μn4(2,1):
      CurrentBestMap
      =n4(MinMap(n3,2),F)
      =n4(n2(C,D),E,F)
      CurrentBestCost(M) = 2 LUTs
    For: μn4(1,2): Same as μn4(1,1)
      Cost = 2 LUTs (tie)
     MinMap(n4,3) = n4(n2(C,D),E,F)
      MinCost = 2 LUTs

## Slide 21: Chortle: Example
For n=n4 (continued)
  For U=4

## Slide 22: Chortle: Example

## Slide 23: Chortle: Example

## Slide 24: Chortle: Example

## Slide 25: Chortle: Example

## Slide 26: Chortle: Example

## Slide 27: Chortle: Example
  MinMap(n5,4)
    = n5(A,B,n3(C,D,E),F)
      MinCost = 2 LUTs

## Slide 28: Chortle-crf Algorithm
Chortle-crf [Francis91]:
  Developed by Francis et al, University of Toronto in 1991
Inputs:
  SOP representation of a single output function
  K-input LUTs
Procedure:
  Bin packing and dynamic programming
  x28 faster

## Slide 29: Bin Packing Problem
Bin packing problem:
  Placing n objects into a number of bins (at most n bins).
  Each object has a weight (Wj > 0)
  Each bin has a limited capacity (Ci > 0)
  Find the best assignment of objects to bins such that
    The total weight of the objects in each bin does not exceed its capacity
    The number of bins used is minimized
Bin
Obj (j):
Bin (i):
Bin
Bin

## Slide 30: 1-D Bin Packing

## Slide 31: Bin Packing : Formulation
Bin
Obj (j):
Bin (i):
Bin
Bin
  Yi = 1 if bini is used
  Xij = 1 if objectj is assigned to bini

## Slide 32: Chortle-crf Algorithm
Example:
  K = 3
  f = ab + cd
   # of inputs = 4 > K
    Cannot use a single LUT.
  Decomposition:
    f1 = ab,
    f2 = cd,
    f = f1 + f2
  Alternative decomposition:
    f1 = ab,
    f = f1 + cd

## Slide 33: Chortle-crf Algorithm
Map the trees:
  Traverse the network from inputs to output.
  At each node v, a circuit implementing the cone (from v to PIs) is constructed.
    The circuit is called Best Circuit (BC) at v.
Objectives in constructing BC:
  Minimize number of LUTs (area)
  Maximize number of unused inputs at the output LUTs
    Allows subsequent nodes to be implemented without extra LUTs.

## Slide 34: Chortle-crf Algorithm
Example:
  K = 5
  An OR node and its fanin LUTs
f
g
h
i
j

## Slide 35: Chortle-crf Algorithm: Decomposition
Decomposition:
  Goal:
    To construct a tree of LUTs that implements
    both the functions of fanin LUTs and
    a decomposition of the node.
Two Steps:
  Two-level decomposition
  Convert it to multi-level decomposition

## Slide 36: Chortle-crf Algorithm: Decomposition
  Two-level
  Multi-level

## Slide 37: Step 1: Two-Level Decomposition
Packing:
  Combining two LUTs LUT1 (implementing f1) and LUT2 (implementing f2) into a new LUTr that implements the function f = f1 Ø f2, where Ø is the function implemented in the fan-out node (e.g. OR)
    Uses first-fit decreasing (FFD) method
    Can use best-fit (BFD)

## Slide 38: Two-Level Decomposition
Bin packing:
  Bins:
    Combined lookup tables
  Objects:
    Fanin lookup tables
  The capacity of each bin:
    K
  Size of each object:
    Number of used inputs of fanin LUT
Example (K=5):
  sizes
    3, 2, 2, 2, 2
  Final contents of the packed bins:
    5, 4, 2

## Slide 39: Chortle-crf: Multi-Level Decomposition
Multi-level Decomposition
  The first-level node is implemented with a tree of LUTs:
    Inputs to the LUT of the 1st-level tree = outputs of the 2nd-level LUTs of two-level decomposition
  Reduction of the number of LUTs:
    by using unused pins of the 2nd-level LUTs to implement a portion of the 1st -level LUTs.
1st level
2nd level
Algorithm MultiLevel
{
while there are more than one unconnected LUT do
{
if there are no free inputs among
the remaining unconnected LUT
{
create an empty LUT and add
it to the end of the LUT list
}
connect the most filled unconnected LUT
to the next unconnected LUT with a free input
}
}
X

## Slide 40: Chortle-crf: Reconvergent Paths
Exploiting reconvergent paths (RP)
  If two boxes share the same input, there is a pair of RPs
  If # of distinct inputs to these two boxes <= K
     can pack into one bin.
f
g
h
i
j
Y
Y
Y

## Slide 41: Chortle-crf: Reconvergent Paths
bin
boxes
K = 3

## Slide 42: Chortle-crf: Logic Replication
Improvement
  Logic replication at fan-out nodes reduces the number of LUTs
    Previous version of Chortle partitioned the circuit into fanout-free trees.

## Slide 43: Chortle-d
Chortle-d:
  Considers delay as objective
  FlowMap solves it optimally.

## Slide 44: References
  [Bobda07] C. Bobda, “Introduction to Reconfigurable Computing: Architectures, Algorithms and Applications,” Springer, 2007.
  [Francis90] R. Francis, J. Rose, K. Chung, “Chortle: A Technology Mapping Program for Lookup Table-Based Field-Programmable Gate Arrays,” DAC 1990.
  [Francis91] R. Francis, J. Rose, Z. Vranesic, “Chortle-crf: Fast technology mapping for lookup table-based FPGAs,” DAC, 1991.

## Slide 45
  Reconfigurable Computing, lecture slides, lect05-ece697f.ppt
  [Lockwood06] J. Lockwood, “Switching Theory,” Lecture slides, Washington University, http://www.arl.wustl.edu/~lockwood/class/cse460/ 2006.
  [Sedgewick83] R. Sedgewick, Algorithms, Addison-Wesley, 1983.
  [Lim08] S. Lim, “Practical Problems in VLSI Physical Design Automation,” Springer, 2008.
  [Trick] Michael A. Trick, “A Tutorial on Dynamic Programming”, http://mat.gsia.cmu.edu/classes/dynamic/dynamic.html