## Slide 1: FPGA Technology Mapping Algorithms
FlowMap

## Slide 2: FlowMap
Objective:
  Minimizing signal delays of mapped designs
    First polynomial-time depth-optimal algorithm
Real signal delay:
  Delay in the LUTs
  Interconnection delay
LUT placement is not known
   Only LUT delay is considered
   Interconnection delay:
    Assumed to be the same for all signals
   The delay of a signal = the number of LUTs that the signal traverses on a path from input to output
 Minimization of the depth of the DAG
Two Steps:
  Node labelling
  Node mapping

## Slide 3: Mapping for Area
Optimizing for area vs. optimizing for delay
  Reducing LUTs (area) may increase delay
Based on network flow problem
4-LUTs

## Slide 4: Mapping for Area
Optimizing for area vs. optimizing for delay
  Reducing LUTs (area) may increase delay
Based on network flow problem
Area = 3
Delay = 3
Area = 4
Delay =2
4-LUTs

## Slide 5: Network Flow Problem
Input:
  A network with a single source (say, an oil field) and a single destination (say, a large refinery)
  All of the pipes ultimately connected to them
Problem:
  What switch settings will maximize the amount of oil flowing from source to destination?

## Slide 6: Network Flow Problem
Assumptions:
  Pipes: fixed capacity (proportional to their size)
  Oil can flow: only in the direction indicated
  Switches at each junction: control how much oil goes in each direction.
The system reaches a state of equilibrium
  Oil flowing in = Oil flowing out
    No matter how the switches are set

## Slide 7: Network Flow Problem
Goal:
  Maximize this amount of flow

## Slide 8: Network Flow Problem
How can switch settings affect the total flow?
  Suppose all switches are open.
     Diagonal pipes are full
    ~ half of the input pipe capacity is used

## Slide 9: Network Flow Problem
How can switch settings affect the total flow?
  Suppose upward pipe is shut-off
    Substantial Increase in total flow into and out of the network.

## Slide 10: Graph Model of Network Flow
Graph model:
  Weighted directed graph
  Nodes:
    Source (with no input edge)
    Sink (with no output edge)
    Pipe junctions
  Edges:
    Pipes
    Directions: oil flow
    Weights:
      flow on edge / pipe capacities
    Flow in a node = Flow out of it
Network flow problem:
  Maximize flow out of the output node

## Slide 11: Graph Model of Network Flow
Graph model:
  Edges can be viewed in both directions:
    (x  y), capacity s, flow f =
    (y  x), capacity -s, flow -f
2/5

## Slide 12: Ford-Fulkerson Method
FF Algorithm:
  Start with a zero flow
  Try to increase flow repeatedly
  Repeat until no increase possible
     Maximum flow found
2/5
0/5
0/3
0/2
0/6
0/4
  Increase flow along the path ADEBCF

## Slide 13: Ford-Fulkerson Method
  Increase flow along the path ABCDEF
2/5
2/2

## Slide 14: Ford-Fulkerson Method
  Increase flow along the path ABCF
2/2

## Slide 15: Ford-Fulkerson Method
  Increase flow along the path ABEF
Condition to stop:
  For all paths from source to destination:
    at least one of the forward edges becomes full or
    at least one of the backward edges becomes empty

## Slide 16: Maxflow-Mincut Theorem
Cut:
  Go through the network (from source to sink) and find the first full forward edge or empty backward edge on every path.
Maxflow-Mincut Theorem:
  Whenever the cut flow equals the total flow, we know not only that the flow is maximal, but also that the cut is minimal.
    Count only the forward edges in cut.
5
3
2
6
4
5
8
2

## Slide 17: Dynamic Programming

## Slide 18: Dynamic Programming
Optimization Technique:
  Procedure:
    Computes and records solutions to all sub-problems proceeding from smallest to largest sub-problem.
      Recording the solution to each sub-problem eliminates the need to recalculate it as part of the solution of any larger sub-problem.

## Slide 19: Dynamic Programming
Example:
  Shortest path problem
    From A to J
    Levelized network:
      A
      B, C, D
      E, F, G
      H, I
      J
[Trick]

## Slide 20: Dynamic Programming
  Shortest distance from node S to the destination J

## Slide 21: Dynamic Programming
  Stage 4:
    F4(H) = 3
    F4(I) = 4
  Stage 3:
3
4
4,H
7,I
6,H

## Slide 22: Dynamic Programming
  Stage 2:
  Stage 1:
3
4
4,H
7,I
6,H
11,E
7,E
8,F
10
10

## Slide 23: Definitions
Fan-in of v: input(v):
  The set of nodes whose outputs are inputs of v
Fan-out of v: output(v):
  The set of nodes which use the output of v as inputs
Primary Input:
  A node with no predecessor
Primary output:
  A node with no successor
Level of a node:
  The length of the longest path from PI to that node
Depth of a graph:
  The largest level of any node in the graph
K-bounded Boolean network:
  if |input(v)|≤ K for all nodes in the graph

## Slide 24: Definitions
  Fanin/fanout
  PI/PO
  Node level, graph depth
  4-bounded?

## Slide 25: Definitions
Tree (fanout-free circuit):
  node v, max(fanout(v)) =1
Forest:
  An independent set of trees

## Slide 26: Definitions
Cone Cv at node v:
  The tree (better to say DAG) with root v which spans from v to a set of inputs: input(Cv)
K-feasible cone :
  Cv is K-feasible at node v if:
    |input(Cv)| ≤ K and
    any path connecting a node in Cv and v lies entirely in Cv
Fanout-free cone:
  Fanouts of every node (other than the root) are inside the cone
A K-feasible Cone at v
  For each node ν, there is a unique maximum fanout-free cone (MFFCv)
  i.e. contains every fanout-free cone rooted at ν
  Spans to PIs

## Slide 28: Basics of Network Flow
FlowMap: a network flow-based method.
Basics of network flow:
Given a network N = (V, E) (a graph) with a source s and target t
  Cut: a partition (X,Xb) of N with s X and t  Xb
  Edge cut-size e(X,Xb): weighted sum of crossing edges
  Node cut-size n(X,Xb) of a cut (X,Xb): # of nodes in X adjacent to some nodes in Xb
  K-feasible cut: iff n(X,Xb) ≤ K
  input(Cv):
    Set of distinct nodes outside of
    Cν supplying inputs to gates in Cν.
a
b
c
d
e
v
PIs

## Slide 29: Basics of Network Flow
29
 Cν is K-feasible if |input(Cν)| ≤ K.
a
b
c
d
e
v
Fv
3-feasible cone Cv
PIs
[Chen04]
3-feasible cut
Notes: 29

## Slide 30: Basics of Network Flow
K-LUT:
  Xb is a K-LUT that implements ν with the inputs to the cone.
We use cuts, cones, and LUTs interchangeably
t-bounded Boolean network:
  if |input(ν)| ≤ t for each node ν
  For Flowmap, the input network must be 2-bounded
    Otherwise, it should be decomposed before Flowmap

## Slide 31: Basics of Network Flow: Example
a
b
c
d
e
v
3-feasible cone Cv
PIs
Delay of 2

## Slide 32: FlowMap: Basic Approach
Node labelling:
  Labels every node in a topological order
  Each node is processed after all its predecessors
  Label:
    Minimum possible depth of the node in any mapping solution
  Dynamic Programming:
    Starting from PI nodes, compute node labels in topological order:
    Compute the label of a node based on labels of its predecessors
Labels of PO nodes:
  Depth of the optimal mapping solution

## Slide 33: FlowMap Algorithm

## Slide 34: FlowMap Algorithm

## Slide 35: FlowMap: Node Labelling
Node labelling:
Steps:
  For a given node t, the cone Ct is transformed into a network Nt :
    Inserting a source node s whose output is connected to all inputs of Nt.
  l(primary input) = 0
  Other nodes’ labels: ?
Network transformation

## Slide 36: FlowMap: LUT Mapping
Lemma:
  If p is the maximum label in input(t), then
  l(t) = p OR
  l(t) = p+1
Algorithm:
  Check whether there is a K-feasible cut (X,Xb) of height p−1 in Nt.
  If yes, then
    l(t)  p and the node t will be packed (in the second phase) in a common LUT with the nodes in Xb.
  If no, then
    the minimum height of the K-feasible cuts in Nt is p and
    Nt − {t} , {t} is such a cut.
    l(t)  p + 1 and
    a new LUT will be used for t.
New Problem:
  How to find out if a network has a K-feasible cut with a given height h.

## Slide 37: Network Collapsing
Network Collapsing:
  Collapses all the nodes in Nt with max-label = p together with t in a new node t’.
Lemma:
  If N’t has a K-feasible cut, Nt has a K-feasible cut of height p − 1
Network collapsing
Nt
N’t

## Slide 38: Node Splitting
  Finding min height K-feasible cut (in Nt)  finding K-feasible cut in N’t
Question:
  How to know if there is a K-feasible cut in N’t?
Answer:
  Network flow algorithms
  Problem:
    They use edge cut optimization
  Solution:
     Node splitting

## Slide 39: Node Splitting
Transform N’t to N’’t:
  For each node v in N’t (except s and t’)
    Introduce v1 and v2
    Connect them by bridging edge (v1, v2)
  s and t’ appear in N’’t too.
    For each (s, v), create a (s, v1)
    For each (v, t’), create a (v2 ,t’)
  For each (u, v) in N’t (u ≠ s and v ≠ t’),
    Create (u2, v1)
    Set capacity:
      1 for bridging edges
       for non-bridging edges
v
v2
v1
1
∞
∞
∞
u
u2

## Slide 40: Node Splitting
Second
transformation

## Slide 41: Node Splitting
N’t to N’’t transformation:
  Ensures that if a cut exists in N’’t with capacity < K, then no edge with infinite capacity will be a crossing one.
  Only bridging edges are crossing the cut
    A LUT may have fanout > 1
       Min-cut in N’t may not work properly
Lemma:
  If N’’t has a cut with edge cut size ≤ K, N’t has a K-feasible cut.

## Slide 42: Example
Example:
  K = 3

## Slide 43: Example
  l(i) = 0 for all PIs
  p = 0
  Topological order: {a, b, c, d, e, f, g, h, i, j, k}
  Not possible to find a cut in N’’a with a cutsize smaller or equal to K = 3
     Xb = {a}
    l(a) = p + 1 = 1.

## Slide 44: Example
Nodes b and c:
  Similar to the case for node a,
Node b:
  Xb = {b},
    l(b) = 1
Node c:
  Xb = {c}
    l(c) = 1

## Slide 45: Example
Node d:
  p = 1
  Max flow (min-cut) = 3
  Xb = {a, d}
  l(d) = p = 1

## Slide 46: Example
Node e:
  Similar to a
  Xb = {e}
  l(e) = 1
Node f:
  similar to d
  Xb = {c, f}
  l(f) = 1

## Slide 47: Example
Node g:
  Xb = {c, g}
  l(g) = p = 1

## Slide 48: Example
Node h:
  Xb = {a, d, h}
  l(h) = l(d) = 1

## Slide 49: Example
Node i:
  N’’i does not contain a K-feasible cut.
  Xb = {i}
  l(i) = p + 1 = 2

## Slide 50: Example
Node j:
  Only one K-feasible cut in N’’j
  Its height is 1.
  Xb = {i, j}
  l(j) = p = 2

## Slide 51: Example
Node k:
  Only one K-feasible cut in N’’k
  Its height is 1.
  Xb = {i, k}
  l(k) = p = 2

## Slide 52: FlowMap Algorithm

## Slide 53: Example
Labels and clusters 
  L = {h, j, k}

## Slide 54: Example
  Remove h from L
  h’ = K-LUT implementation of h
  Table: h’ contains {a, d, h}

## Slide 55: Example
  input(h’) contains three PI nodes
  We do not add PI nodes into L
   L = {j, k}

## Slide 56: Example
  Remove j from L
  Table: j’ contains {i, j}
  input(j’) = {e, b, f}
   L = {k}  {e, b, f} = {k, e, b, f}

## Slide 57: Example
  Remove k from L
  Table: k’ contains {i, k}
  input(k’) = {b, f, g}
   L = {e, b, f}  {b, f, g} = {e, b, f, g}

## Slide 58: Example
  Remove e from L
  Table: e’ contains {e}
  input(e’) = PI nodes
   L = {b, f, g}

## Slide 59: Example
  Remove b from L
  Table: b’ contains {b}
  input(b’) = PI nodes
   L = {f, g}

## Slide 60: Example
  Remove f from L
  Table: f’ contains {c, f}
  input(f’) = PI nodes
   L = {g}

## Slide 61: Example
  Remove g from L
  Table: g’ contains {c, g}
  input(g’) = PI nodes
   L = Ø

## Slide 62: Example
7 K-LUTs generated

## Slide 63: Example
Max label = 2
   Max delay = 2

## Slide 64: References
  [Cong94] J. Cong and Y. Ding, “Flowmap: an optimal technology mapping algorithm for delay optimization in lookup-table based fpga designs,” IEEE Trans. on CAD of Integrated Circuits and Systems, vol. 13, no. 1, pp. 1–12, 1994.
  [Sedgewick83] R. Sedgewick, Algorithms, Addison-Wesley, 1983.
  [Lim08] S. Lim, “Practical Problems in VLSI Physical Design Automation,” Springer, 2008.