## Slide 1: Software Defined Networking and Open Flow Protocol
Theophilus Benson

## Slide 2: Outline
Section 1: SDN Ecosystem
  SDN Motivation
  SDN Primer
  Dimensions of SDN Environments
  Dimensions of SDN Applications
Section 2: OpenFlow Primer

## Slide 3: Section 1

## Slide 4: Network Today…
Vertical integrated stacks
  Similar to PC in 1980s
IBM’s Mainframe
Cisco Routers
D.B.
O.S
CPU
COBOL Apps.
VLANS
Switch O.S.
ASIC
L3 Routing

## Slide 5: Implications of Networking…
Restricted to ill defined vendor CLI
  Provisioning is slow….
    VM provisioning: 1min
    Virtual network provisioning: 1-3 weeks

## Slide 6: Background: Switch Internals
Logical View of a Switch
Physical Architecture of a Switch
Switching
Fabric
Processor
ASIC
AISC
data plane
control plane
Network O.S.
ASIC
Applications
Applications

## Slide 7: Software Defined Networking
Southbound API: decouples the switch hardware from control function
  Data plane from control plane
Switch Operating System: exposes switch hardware primitives
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
Network O.S.
ASIC
Applications
Applications
Current Switch
Vertical stack
SDN Switch
Decoupled stack

## Slide 8: Implications Of SDN
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Global View
Programmatic
Control
Current Networking
SDN Enabled Environment
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 9: Implications Of SDN
Current Networking
SDN Enabled Environment
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Distributed protocols
  Each switch has a brain
  Hard to achieve optimal solution
Network configured indirectly
  Configure protocols
  Hope protocols converge
Global view of the network
  Applications can achieve optimal
Southbound API gives fine grained control over switch
  Network configured directly
  Allows automation
  Allows definition of new interfaces
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications
Network O.S.
ASIC
Applications
Applications

## Slide 10: How SDN Works
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S

## Slide 11: How to Pick an SDN Environment
Network O.S.
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware
What is the Southbound AP!?
Is the switch hardware and OS closed?
Is the switch virtual or physical?
How easy is it to develop on for the
Controller platform?

## Slide 12: The SDN Stack
Controller
NOX
Slicing
Software
FlowVisor
FlowVisor
Console
12
Applications
LAVI
ENVI (GUI)
…
n-Casting
NetFPGA
Software
Ref. Switch
Broadcom
Ref. Switch
OpenWRT
PCEngine WiFi AP
Commercial Switches
OpenFlow
Switches
…
Monitoring/ debugging tools
oflops
oftrace
openseer
Open vSwitch
HP, IBM, NEC, Pronto, Juniper.. and many more
Beacon
Trema
FloodLight
Source: SDN Tutorial by B. Heller
Open Networking Summit, April 2012
Notes: There are components at different levels that work together in making it work

## Slide 13: Dimensions of SDN Environments: Vendor Devices
Vertical Stacks
Vendor bundles switch and switch OS
  Restricted to vendor OS and vendor interface
Low operational overhead
  One stop shop
Whitebox Networking
Vendor provides hardware with no switch OS
Switch OS provided by third party
  Flexibility in picking OS
High operational overhead
  Must deal with multiple vendors

## Slide 14: Dimensions of SDN Environments: Switch Hardware
Virtual: Overlay
Pure software implementation
  Assumes programmable virtual switches
  Run in Hypervisor or in the OS
  Larger Flow Table entries (more memory and CPU)
Backward compatible
  Physical switches run traditional protocols
Traffic sent in tunnels
  Lack of visibility into physical network
Physical: Underlay
Fine grained control and visibility into network
Assumes specialized hardware
  Limited Flow Table entries

## Slide 15: Dimensions of SDN Environments: Southbound Interface
OpenFlow
Flexible matching
  L2, L3, VLAN, MPLS
Flexible actions
  Encapsulation: IP-in-IP
  Address rewriting:
    IP address
    Mac address
BGP/XMPP/IS-IS/NetConf
Limited matching
  IS-IS: L3
  BGP+MPLS: L3+MPLS
Limited actions
  L3/l2 forwarding
  Encapsulation

## Slide 16: Dimensions of SDN Environments: Controller Types
Modular Controllers
Application code manipulates forwarding rules
  E.g. OpenDaylight, Floodlight
Written in imperative languages
  Java, C++, Python
Dominant controller style
High Level Controllers
Application code specifies declarative policies
  E.g. Frenetic, McNettle
Application code is verifiable
  Amendable to formal verification
Written in functional languages
  Nettle, OCamal

## Slide 17: BigSwitch
Controller Type
  Modular: Floodlight
Southbound API: OpenFlow
  OpenFlow 1.3
SDN Device: Whitebox
  (indigo)
SDN Flavor
  Underlay+Overlay

## Slide 18: SDN EcoSystem
Arista
OF + proprietary
Underlay
Vertical Stack
Broadcom
OF + proprietary
Underlay
Vertical Stack
HP
OF
Underlay
Vertical Stack
Cisco
OF + proprietary
Underlay+Overlay
Vertical Stack
FloodLight
OF
Underlay+Overlay
Whitebox
Dell
OF
Underlay
Vertical Stack
HP
OF
Underlay
Vertical Stack
Alcatel
BGP
Overlay
Vertical Stack
Juniper
BGP+NetConf
Overlay
Vertical Stack

## Slide 19: SDN Stack
Southbound API: decouples the switch hardware from control function
  Data plane from control plane
Switch Operating System: exposes switch hardware primitives
Controller (Network O.S.)
Applications
Applications
Applications
Southbound
API
SDN
Switch Operating System
Switch Hardware

## Slide 20: Section2: Southbound API: OpenFlow

## Slide 21: OpenFlow
Developed in Stanford
  Standardized by Open Networking Foundation (ONF)
  Current Version 1.4
    Version implemented by switch vendors: 1.3
Allows control of underlay + overlay
  Overlay switches: OpenVSwitch/Indigo-light
PC

## Slide 22: How SDN Works: OpenFlow
Controller (N. O.S.)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S
OpenFlow
OpenFlow

## Slide 23: OpenFlow: Anatomy of a Flow Table Entry
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Match
Action
Counter
Forward packet to zero or more ports
Encapsulate and forward to controller
Send to normal processing pipeline
Modify Fields
When to delete the entry
VLAN
pcp
IP
ToS
Priority
Time-out
What order to process the rule
# of Packet/Bytes processed by the rule

## Slide 24: OpenFlow: Types of Messages
Asynchronous (Controller-to-Switch)
  Send-packet: to send packet out of a specific port on a switch
  Flow-mod: to add/delete/modify flows in the flow table
Asynchronous (initiated by the switch)
  Read-state: to collect statistics about flow table, ports and individual flows
  Features: sent by controller when a switch connects to find out the features supported by a switch
  Configuration: to set and query configuration parameters in the switch
Asynchronous (initiated by the switch)
  Packet-in: for all packets that do not have a matching rule, this event is sent to controller
  Flow-removed: whenever a flow rule expires, the controller is sent a flow-removed message
  Port-status: whenever a port configuration or state changes, a message is sent to controller
  Error: error messages
Symmetric (can be sent in either direction without solicitation)
  Hello: at connection startup
  Echo: to indicate latency, bandwidth or liveliness of a controller-switch connection
  Vendor: for extensions (that can be included in later OpenFlow versions)

## Slide 25: Dimension of SDN Applications: Rule installation
Proactive Rules
Reactive Rules
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 26: Dimension of SDN Applications: Rule installation
Proactive Rules
Controller pre-installs flow table entries
  Zero flow setup time
Requires installation of rules for all possible traffic patterns
  Requires use of aggregate rules (Wildcards)
  Require foreknowledge of traffic patterns
  Waste flow table entries
Reactive Rules
First packet of each flow triggers rule insertion by the controller
  Each flow incurs flow setup time
  Controller is bottleneck
  Efficient use of flow tables

## Slide 27: Dimensions of SDN Applications: Granularity of Rules
Microflow
WildCards (aggregated rules)
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S

## Slide 28: Dimensions of SDN Applications: Granularity of Rules
Microflow
One flow table matches one flow
Uses CAM/hash-table
  10-20K per physical switch
Allows precisions
  Monitoring: gives counters for individual flows
  Access-Control: allow/deny individual flows
WildCards (aggregated rules)
One flow table entry matches a group of flow
Uses TCAM
  5000~4K per physical switch
Allows scale
  Minimizes overhead by grouping flows

## Slide 29: Dimensions of SDN Applications: Granularity of Rules
Distributed Controller
Centralized Controller
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Switch O.S
Switch HW
Switch O.S
Switch HW
Switch O.S
Switch HW
Controller (N. O.S.)
Applications
Applications
Applications
Controller (N. O.S.)
Applications
Applications
Applications

## Slide 30: Google’ B4 Application
Rule installation
  Proactive
Rule Granularity
  Aggregate
Distributed
  Multiple instances

## Slide 31: OpenFlow: Message Formats
Controller encapsulates message into an object
  Accessor functions to different fields
  No need to worry about crafting network packets

## Slide 32: OpenFlow Actions (Partial list from OpenFlow 1.0 spec)
Output to switch port (Physical ports & virtual ports). Virtual ports include the following:
  ALL (all standard ports excluding the ingress port) - flood
  CONTROLLER (encapsulate and send the packet to controller) – PACKET_IN message
  LOCAL (switch’s stack) – go through the IP layer, etc (mostly used for vSwitches)
  NORMAL (process the packet using traditional non-OpenFlow pipeline of the switch) – traditional L2 forwarding, L3 routing
Drop
Set fields (packet modification/header rewriting)
  Ethernet Source address
  Ethernet Dest address
  IP source & dest addresses, IP ToS, IP ECN, IP TTL, VLAN
  TCP/UDP source and destination ports
Strip (pop) the outer VLAN tag
Set queue ID when outputting to a port (Enqueue)
New in OpenFlow 1.1+
  Support for matching across mulitple tables
  Support for tunneling
  Support for Push/Pop mulitple VLAN/MPLS/PBB tags

## Slide 33: Conclusion
An overview of SDN technologies
Introduction to OpenFlow