## Slide 1: In-System Integration

## Slide 2: Types of Using Reconfigurable Devices
Reconfigurable devices (RD) are usually used in three different ways:
  Rapid prototyping
  Non-frequently reconfigurable systems
  Frequently reconfigurable systems

## Slide 3: 1. Rapid Prototyping
  The RD is used as emulator for a circuit to be produced later as ASIC.
  The emulation process allows for testing the correctness of the circuit, before production.
  Reconfiguration only when a new implementation of ASIC is needed.

## Slide 4: 2. Non-Frequent Reconfiguration
  The RD is used as application specific device similar to ASIC.
  Possibility of upgrading the system by means of reconfiguration.
  Configuration usually in EEPROM/flash.
  No reconfiguration during operation.

## Slide 5: 3. Frequent Reconfiguration
  Usually coupled with a processor
  RD is used as an accelerator for time-critical parts of applications.
  The processor accesses the RD using function calls.
More and more stand-alone frequently reconfigurable systems are appearing.

## Slide 6: Classification: Proximity
Degree of Coupling with CPU:
  Reconfigurable fabric as a standalone device
    Communication by existing CPU I/O mechanism.
    Slow data transfer
       Applications in which a significant amount of processing can be done by the fabric without processor intervention.
      E.g. emulation systems: (Cadence Palladium, Mentor’s Vstation Pro)
[Todman05]
[Compton02]

## Slide 7: Classification: Proximity
Degree of Coupling with CPU:
  As an attached processing unit/co-processor
    Acts as an extra processor in a multi-processor system/co-processor.
    Host and the reconfigurable logic can execute simultaneously.
    Cost of communication is lower
    Cannot/can see the host’s Cache
  Examples:
    PipeRench
    Garp
    MorphoSys
    PAM
    OneChip

## Slide 8: Classification: Proximity
Degree of Coupling with CPU:
  As a functional unit
    Very tightly-coupled
    RFUs execute as functional units on the main microprocessor datapath,
    Registers used to hold the input and output operands
    RFU allows custom instructions (may change over time)
  Examples:
    MATRIX
    RAW

## Slide 9: Classification: Proximity
Degree of Coupling with CPU:
  CPU embedded in reconf fabric
    Hard core
    Soft core

## Slide 10: Proximity: Summary
Tighter Coupling:
  Lower communication overhead
    Reconf. h/w can be used more frequently within an application.
  Reconf. h/w is unable to operate for significant portions of time without intervention of host.
  Amount of reconfigurable logic available often limited.
Looser Coupling:
  Greater parallelism in program execution,
  Higher communications overhead.

## Slide 11: Classification: Proximity

## Slide 12: Terminology

## Slide 13: Static and Dynamic Reconfiguration
  Offline Reconfigurable System
  (static)
  Run-time reconfigurable systems
  Static
  Dynamic

## Slide 14: Offline vs. Run-Time Reconfiguration

## Slide 15: Static and Dynamic Reconfiguration
  Off-line static reconfigurable systems
    The computation and reconfiguration is defined once at compile time.
    No reconfiguration during run-time

## Slide 16: Static and Dynamic Reconfiguration
  Run-time static reconfigurable systems
    The computation and reconfiguration is defined once at compile time
    The computation and reconfiguration sequences are known at compile-time
    Reconfiguration during run-time

## Slide 17: Static and Dynamic Reconfiguration
  Run-time dynamic reconfigurable systems
    The computation and reconfiguration sequences are not known at compile-time.
    The system reacts dynamically at run-time to computation.

## Slide 18: References
[Bobda07] C. Bobda, “Introduction to Reconfigurable Computing: Architectures, Algorithms and Applications,” Springer, 2007.
[Todman05] T.J. Todman, G.A. Constantinides, S.J.E. Wilton, O. Mencer, W. Luk and P.Y.K. Cheung, “Reconfigurable computing: architectures and design methods,” IEE Proceedings, 2005.
[Compton02] K. Compton, S. Hauck, “Reconfigurable Computing: A Survey of Systems and Software, ACM Computing Surveys,” Vol. 34, No. 2, June 2002, pp. 171–210.